1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Smoke System, Landing

Takeoff
1. Elevator Trim ... -1.5 deg (indicator on upper left instrument panel, down 1.5 lines)
2. Flaps ... TAKE OFF (middle switch position)
3. Engine Ignition Switch ... CONT IGN (aft position) (just in front of throttle)
4. Brakes will hold full mil power.
5. Begin takeoff run. Use differential brakes up to 40 kts, rudder after that.
6. Rotate at approx 110-130 kts, heavier is faster.
7. Retract gear before 200 kts.
8. Retract flaps before 190 kts.
9. Engine Ignition Switch ... OFF (middle position)
10. Throttle back to maintain 795 dec C ITT (max continuous).

Smoke System
1. White Smoke and Colour Smoke circuit breakers ... IN (left console outboard)
2. Press Red Button to toggle smoke system on/off. Smoke system always produces white smoke.
3. When smoke system is on, press Trigger to add red or yellow colorant (as equipped) to the white smoke, making it that color.
4. System status is shown with lights on instrument panel top center.

Landing
Landing gear warning horn sounds when under 75% N1 (slightly over 50% physical throttle) and gear is not down. Cannot be canceled (I think??) but volume can be adjusted with INT knob on AUDIO panel.
1. Engine Ignition Switch ... CONT IGN (aft position) (just in front of throttle)
2. Speedbrakes ... Out full, and keep out through landing
3. Under 200 kts: Landing gear ... Down
4. Under 190 kts: Flaps ... TAKE OFF (middle switch position)
5. Under 150 kts: Flaps ... DOWN FULL (bottom switch position)
6. Slow to On Speed AOA (approx 120 kts, no AOA indicator) and trim.
7. Adjust pitch with throttle.
8. Aim at end of runway. Approach angle/glideslope should be 3°.
9. Cut throttle at runway threshold, flare at 110 kts, touchdown at 95 kts, aerobrake until nose drops.
10. After stopping, retract airbrake, set flaps to up, and Engine Ignition Switch ... OFF (middle position).