1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Cold Start - RIO

Cold Start Checklist for RIO -- WIP, needs verification and more steps (Auto Start is as fast or faster)
1. Wait for ground power and air supply on.
2. OXYGEN switch ... ON (forward) (left console extreme rear)
3. WCS ... Standby (switch on center console, right of HCU stick)
  - Takes about 40 seconds for the displays to turn on.
1. Data link ... On (right console forward outboard)
2. Data link MODE switch ... CAINS/WAYPT (not sure if only for carrier, or on ground also) (right console forward)
3. Align INS:
  1. If on ground:
    1. TID NAV MODE knob ... GND (above left of TID display)
    2. Enter Lat/Long and altitude:
      1. Starting lat/long is on kneeboard page.
      2. On KEYBOARD to left of seat, press CLEAR, 1 for latitude, N+E once for North, then latitude in DD MM S format. Verify value at top of TID, then press ENTER on KEYBOARD.
      3. Press 6 for longitude, N+E once for East, then longitude in DD MM S format. Verify value at top of TID, then press ENTER on KEYBOARD.
      4. Press 4 for altitude, enter current altitude in ft, verify value at top of TID, then press ENTER.
  2. If on carrier:
    1. TID NAV MODE knob ... CVA (above left of TID display)
  3. If you have stored alignment, TID will say ASH (Automatic Stored Heading), and KEYBOARD panel will have arrow next to STORED HDG ALIGN when CATEGORY knob is set to NAV. Alignment is much faster (~2 mins) with stored alignment, but all steps above must still be followed.
  4. While waiting for alignment to complete, continue with the checklist.
  - Caret on top moves from left to right as INS aligns, takes about 7 minutes on ground, 9 minutes on carrier, 2 minutes if using stored alignment.
  - Number on left is tenths of minutes that the alignment has been running (e.g. 5 minutes = 50)
  - First tick mark is Coarse Alignment Complete, and aircraft can be flown, but Sparrow and Phoenix will only work in boresight modes.
  - Second tick mark is Alert Launch Criteria, and allows Sparrow and Phoenix non-boresight modes. Caret becomes a diamond at this tick.
  - Third tick mark is Fine Alignment Complete, and indicates full accuracy alignment. Caret becomes a dotted diamond at this tick.
1. TACAN ... T/R (left console)
2. Radio ... T/R+G (left console)
3. Liquid Cooling Switch ... ON (left console rear outboard)
4. Set armament panel switches to SAFE (down) (front left panel)
5. Backup ADI ... Uncage (left click knob) (left side of instrument panel)
6. RWR receiver ... On (right console forward)
7. DECM ... STBY (right console forward)
8. IFF ... On (right console middle outboard)
9. When INS alignment complete: TID NAV MODE knob ... INS
10. Data link MODE switch ... TAC (right console forward)

Proceed with rest of preflight checklist on next page.