1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

203 - Ground - Preflight, Performance Limits

Preflight (after cold start or from hot start) -- WIP
1. BINGO fuel ... As needed (default is 4000 lbs) (fuel panel above right knee)
2. Radios ... As needed
3. Data link ... Tune to AWACS (use Jester menu)
4. ROUNDS counter ... 680 (you actually have 676 rounds) (right instrument panel, next to Hook handle)
5. If using Laser Guided Bombs, set laser code for bombs in the built-in kneeboard pages.

Performance limits
- Fuel: 16200 lbs internal
  - with 2x external tanks (2003 lbs ea.) = 20205 lbs
  - Ground refueling time: ~2,600 lbs/min, 6m04s to fill from empty
- Flaps: 225 kts
- Landing Gear: 250 kts
- Flat spin recovery:
  - Rudder against spin.
  - Full stick forward.
  - Full power on engine on inside of spin, idle power on engine on outside of spin.
  - When plane noses down and stops spinning, both engines to idle, center controls, slowly increase throttle and pull up.