1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Navigation, Autopilot, Jettison, Radios

Waypoints -- WIP
- Waypoint types:
  - WPT1, WPT2, WPT3 -- Up to 3 navigation waypoints
  - FP -- Fixed Point, used for INS updates
  - IP -- Initial Point, for bombing run
  - ST -- Surface Target, ground target location
  - DP -- Defended Point, friendly ground location
  - HA -- Hostal Area, known enemy location
  - HB -- Home Base, location of carrier or home airfield
  - Special datalink waypoints: DLWP1, DLWP2, DLWP3, DLST, DLFP
1. Navigate to waypoint:
  1. Jester: Navigation > Select Destination Steer Point > (select waypoint)
  2. HSD Mode switch ... NAV
  3. STEER CMD button ... DEST
2. Add waypoints with F10 map and Jester:
  1. Add marker to F10 map. Label doesn't matter, but should not be blank.
  2. Open Jester menu > Navigation > Steer Point From Map > (select waypoint you want to set) > (select map marker)

TACAN navigation -- WIP
1. Tune TACAN reciever:
  1. Jester: Navigation > TACAN > Tune Tac > (select TACAN unit)
  2. Or in pilot seat, TACAN panel is on left console rear, set channel, X/Y, and mode, then set TACAN CMD button to PLT.
2. TACAN may take up to 2 minutes to warm up.
3. Display Mode button ... CRUISE (Mode dial 2)
4. STEER CMD buttons ... TACAN (right console bottom)
5. HSD shows a triangle on the outside of the compass wheel indicating direction to TACAN station, "+" is the reciprocal. Top left shows range to TACAN station.
6. HSI compass to right of VDI also shows arrow pointing to TACAN and range in window.

Autopilot and SAS
- To turn on autopilot, all the SAS switches must be on (shift Pinky Switch up/down/press)
- Toggle autopilot switch with Pinky Switch press. That engages attitude hold mode.
  - To turn off with Pinky Switch press, you may have to disengage autopilot altitude or heading hold switches first.
- Pull brake lever to turn off all autopilot functions, as well as disabling roll and pitch SAS. (You may want to turn Pitch SAS back on (shift-Pinky Switch up); only Roll SAS needs to disabled for 15+ AOA flight.)
- To activate altitude hold:
  - Main Autopilot switch ... ON (Pinky Switch press)
  - Altitude hold switch ... ON (Pinky Switch down)
  - A/P REF light will turn on next to VDI.
  - You must be no more than 200 ft/min climb/dive, then press NWS button (Flip Down Trigger) to activate altitude hold. A/P REF light should go out.

Jettison
- Emergency Stores Jettison button on left side of cockpit dumps everything except Sidewinder missiles.
- To jettison drop tanks, use Jester menu, in the WITHIN VISUAL RANGE menu. May have to be flying straight and level, and under Mach 1.
- Check external tank amounts by holding B4 button and checking outer numbers on fuel gauge above right knee.

Radios
COM1	ARC-159 (Pilot)	225.000 to 399.975 MHz AM	--
COM2	ARC-182 (RIO)	30 to 88 MHz FM / 108 to 118 MHz AM / 118 to 156 MHz AM / 156 to 174 MHz FM / 225 to 400 MHz AM/FM	--

- Tune pilot radio with radio panel on left console behind throttle.
- Tune RIO radio with Jester.