1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Landing

Shore Landing
1. ANTI-SKID SPOILER BK switch ... BOTH (front left panel, bottom)
2. HOOK BYPASS switch ... FIELD (right console)
3. Display Mode button ... LDG (front right panel) (Mode dial 5)
4. Wing Sweep ... Auto (shift-Top Hat up)
5. Speed brakes ... Deploy and keep out through landing
6. At 250 kts: Landing gear ... Down
7. At 225 kts: Flaps ... Down
8. After flaps down: DLC (Direct Lift Control) ... Activate (Gray Reset Hat press, flaps must be down)
9. Slow to On Speed AOA, trim to put aircraft reticle ("¬·⌐", not velocity vector) in the center of the "E", approx 140 to 150 kts.
10. Do not flare, fly it down into the ground.
11. After stopping, retract airbrake and flaps.

Carrier Landing -- General visual instructions; for proper Case approaches, see other page
1. Set TACAN to carrier's channel (see steps on other page). May take up to 2 minutes to warm up.
2. Set ICLS to carrier's channel for instrument approach guidance (see steps below).
3. Within 50 nmi, contact carrier and say "Inbound". Carrier will respond with BRC (Base Recovery Course, the heading of the carrier itself). Set that as a Course in the HSD for reference.
4. Call "See you at 10" when 10 miles out.
5. Fly the pattern (left as an exercise to the reader).
6. ANTI-SKID SPOILER BK switch ... OFF (front left panel, bottom)
7. HOOK BYPASS switch ... CARRIER (right console)
8. Display Mode button ... LDG (front right panel) (Mode dial 5)
9. Wing Sweep ... Auto (shift-Top Hat up)
10. Speed brakes ... Deploy and keep out through landing
11. At 250 kts: Landing gear and Hook ... Down (T5 switch and shift T5 switch)
12. At 225 kts: Flaps ... Down
13. DLC (Direct Lift Control) ... Activate (Gray Reset Hat press, flaps must be down)
14. Slow to On Speed AOA, trim to put aircraft reticle ("¬·⌐") in the center of the "E", approx 140 to 150 kts.
15. On final turn, call Tomcat Ball (B6 button) to get LSO guidance.
16. Put VV about at the crotch of the carrier, where the front of the angled deck meets the main flight deck on the port side.
17. Fly it down to an "OK 3-wire".
18. After stopping: retract hook, airbrake, and flaps, and fully sweep wings (shift-Top Hat back).

ICLS landing
1. ICLS panel is on right console forward (ARA-63 control panel)
2. Tune to carrier's ICLS channel and power on.
3. Display Mode button ... LDG (front right panel) (Mode dial 5)
4. HUD AWL switch ... ILS
5. VDI AWL switch ... ILS
6. HSD Mode switch ... NAV
7. STEER CMD button ... AWL/PCD
8. Display switches for HUD AWL and VDI AWL to ILS (front right panel)
9. STEER CMD switch ... AWL/PCD
10. Needles should appear on HUD and VDI.
11. Put aircraft reticle ("¬·⌐") on the center of the needles.

Landing with ACLS (Automatic Carrier Landing System)
See next page