1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Landing with ACLS

Landing with ACLS (Automatic Carrier Landing System) -- WIP
When beginning to return to carrier
1. Set TACAN to carrier's channel (see steps on other page). May take up to 2 minutes to warm up.
2. Set ICLS to carrier's channel for instrument approach guidance (see steps on other page).
3. Set display switches as needed to navigate back to the carrier with TACAN.
At 50 nmi from the carrier
1. Call "Inbound" on radio. Carrier will respond with weather, altimeter setting, and BRC.
2. Use Course knob on HSD to set the carrier's BRC as the Course.
3. Tune data link freq to carrier (find on kneeboard TACTICAL DATALINK SYSTEMS page):
  1. Jester: Data Link/Radio > Set Host/Radio > (select carrier)
4. Fly to intercept BRC course about 15 to 20 nmi aft of the carrier at about 5000 ft. (Usually this will be a Case III recovery, follow Case III recovery steps on other page for general pattern instructions.)
When 15 to 20 nmi aft of the carrier, and roughly aligned with the BRC
1. Set up displays and HUD for ACLS (front right panel):
  1. Display Mode button ... LDG (front right panel) (Mode dial 5)
  2. HUD AWL switch ... ACL
  3. VDI AWL switch ... ACL
  4. HSD Mode switch ... NAV
  5. STEER CMD button ... AWL/PCD
2. ANTI-SKID SPOILER BK switch ... OFF (front left panel, bottom)
3. HOOK BYPASS switch ... CARRIER (right console)
4. Wing Sweep ... Auto (shift-Top Hat up)
When 8 to 10 nmi aft of the carrier
1. Speed brakes ... Deploy and keep out through landing
2. At 250 kts: Landing gear and Hook ... Down (T5 switch and shift T5 switch)
3. At 225 kts: Flaps ... Down
4. DLC (Direct Lift Control) ... Activate (Gray Reset Hat press, flaps must be down)
5. Autopilot VEC/PCD/ACL switch ... ACL (left console, outboard autopilot switch)
6. Autopilot switch ... Engage (left console, or Pinky Switch press)
  - A/P REF light next to VDI will light up.
Throttle Mode switch ... AUTO, then don't touch the throttle (left console outboard of throttle, or Front Thumb Button press)
  - To engage, throttle must be between 75 and 90%, landing gear handle down, no weight on wheels.
  - When engaged, plane should adjust speed to maintain on-speed AOA.
1. Fly to intercept the glide slope.
2. Lights next to VDI will light up as you approach carrier:
  1. LANDING CHK at 6 nmi (indicates carrier is ready and for you to do final landing checks)
  2. ACL READY and A/P CPLR at 4 nmi (indicates carrier landing system has acquired your plane)
When 4 nmi from the carrier, engage ACLS
1. When LANDING CHK, ACL READY, A/P CPLR, and A/P REF lights are lit, press NWS button (Flip Down Trigger) to engage ACLS
2. A/P REF light goes out, CMD CONTROL lights up, plane is now controlled by autopilot.
  - To disengage autopilot at any time, press PLM Button (Middle Finger Hat press).
1. At 10 seconds from touchdown, 10 SECONDS light goes on.
2. Plane flies to a 3-wire, in theory...
3. You need to manually go to MIL power or AB on touchdown.