1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

402 - A/A - Gun and Sidewinder

Master Arm ... ON
Display Mode buttons ... A/A (Mode dial 3)

Best sustained turn ... ~320 kts with maneuvering flaps down (Gray Reset Hat forward)

ACM radar modes
Middle Finger Hat controls ACM modes:
- P: PLM button (Pilot Lockon Mode, press and hold to lock target at boresight within 5 nmi)
- U: Target designate up / VSL HI (Vertical Scan Lockon, 5 deg wide, +15 deg to +55 deg, 5 nmi)
- D: Target designate down / VSL LO (Vertical Scan Lockon, 5 deg wide, -15 deg to +25 deg, 5 nmi)
- R: Target designate forward / PAL (Pilot Automatic Lockon, 20 deg wide 8-bar scan, 15 nm)

Gun
1. Weapon Selector switch ... GUN (Dish Hat up/down)
2. GUN RATE button ... As desired (HIGH recommended) (UFC)
3. With no designated target, crosshair pipper shows gun trajectory at 1000 ft range, diamond pipper shows gun trajectory at 2000 ft range.
4. (Optional) Designate radar target for radar lead computing (use Jester or see above for ACM modes)
  - NOTE: If using PAL lockon mode (Middle Finger Hat right), diamond pipper will not visibly sweep when in gun mode, because it's being used as part of the gun symbology when no target is locked. However the radar is still sweeping as normal, left to right, bottom to top, and diamond will lock onto a target when it gets one.
1. HUD shows closure on left side, range on right side.
2. Put pipper on the target diamond and press Trigger to fire.
  - Gun ammo counter is below the "G" in the HUD (x100 rnds) or on front right console next to the hook lever.

AIM-9 Sidewinder
1. SW COOL button ... ON (takes 60 seconds to fully cool the seekers) (UFC)
2. Weapon Selector Switch ... SW (Dish Hat up/down)
3. MODE/STP buttons ... As desired (NORM = allow uncaged, BRSIT = slaved to centerline) (UFC)
4. (Optional) Designate radar target to slave seeker (use Jester or see above for ACM modes)
5. If using NORM mode, press Uncage button (Rear Thumb Button) to uncage missile for 4.5 seconds to search for targets or slave to radar target. If no target is found, missile will re-cage automatically.
6. VDI shows Max and Min range on vertical line. Put "⊥" mark in center of black ASE circle for best lead.
7. HUD shows closure on left side, range on right side.
8. When you have tone, fire with Trigger.