1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

403 - A/A - Sparrow and Phoenix

Master Arm ... ON
Display Mode buttons ... A/A (Mode dial 3)

Best sustained turn ... ~320 kts with maneuvering flaps down (Gray Reset Hat forward)

ACM radar modes
Middle Finger Hat controls ACM modes:
  - P: PLM button (Pilot Lockon Mode, press and hold to lock target at boresight within 5 nmi)
  - U: Target designate up / VSL HI (Vertical Scan Lockon, 5 deg wide, +15 deg to +55 deg, 5 nmi)
  - D: Target designate down / VSL LO (Vertical Scan Lockon, 5 deg wide, -15 deg to +25 deg, 5 nmi)
  - R: Target designate forward / PAL (Pilot Automatic Lockon, 20 deg wide 8-bar scan, 15 nm)

AIM-7 Sparrow
MSL PREP buttons ... ON (UFC)
  - Takes 2 minutes to warm up missiles. Station indicators above VDI show checkerboards when ready.
1. Weapon Selector switch ... SP / PH (Dish Hat up/down, Dish Hat press to toggle SP or PH)
2. MODE/STP buttons ... As desired
  1. NORM for STT targets
  2. BRSIT for flood mode
3. Acquire target lock.
4. VDI shows Max and Min range on vertical line. Put "⊥" mark in center of black ASE circle for best lead.
5. HUD shows closure on left side, range on right side.
6. When in range, fire with Trigger. Takes a few seconds for the missile to fire after trigger is pressed.

AIM-54 Phoenix
- Missile	Smoke	Range	Weight	Elec.	Speed
- AIM-54A Mk47 (Mod 0)	Yes	3	978 lbs	Analog	2
- AIM-54A Mk60	Yes	1	1040 lbs	Analog	1
- AIM-54C Mk47 (Mod1)	Less	2	1027 lbs	Digital	3
Single target
MSL PREP buttons ... ON (UFC)
  - Takes 2 minutes to warm up missiles. Station indicators above VDI show checkerboards when ready.
1. Weapon Selector switch ... SP / PH (Dish Hat up/down, Dish Hat press to toggle SP or PH)
2. MODE/STP buttons ... As desired
  1. NORM for STT targets
  2. BRSIT for flood mode
3. Acquire target lock.
4. VDI shows Max and Min range on vertical line. Put "⊥" mark in center of black circle for best lead.
5. HUD shows closure on left side, range on right side.
6. When in range, fire with Trigger. Takes a few seconds for the missile to fire after trigger is pressed.
7. Must maintain lock until missile goes active ~16 secs before impact. The "go active" command is sent from the plane; the missile will not go active on its own after a certain amount of time.
TWS multiple targets
TODO