1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Pilot - TPOD, GBU-10/12/16 Paveway II LGBs

Laser Guided Bombs and TPOD use with Jester -- WIP
- Jester will use LANTIRN automatically in A/G mode, and TCS camera in A/A mode. To manually set LANTIRN or TCS in either Display Mode:
  - Jester: Air To Ground/Weapons -> Use TCS/Utility or Use LANTIRN/Utility
1. Master Arm ... ON
2. Display Mode button ... A/G (Mode dial 4)
  - Jester will start warming up the pod when weight-off-wheels. Takes about 9 minutes to warm up.
  - After the pod is warmed up, switching to A/G mode may show NOT RDY in the LANTIRN display, indicating standby mode. May take 30s to 1m to bring the pod out of standby.
VDI DISPLAY MODE switch ... TV to show the LANTIRN display
  - Note that TID repeater will be blank when LANTIRN is active.
Jester: Air To Ground/Weapons, then go through the settings to select and configure bombs as needed. Current configuration is shown in the center of the Jester menu wheel.
  - You should be in MANUAL mode for the drop, although CMP/PLT will also work.
1. Weapon Selector switch ... OFF (Dish Hat down)
2. Selected stations should show checkerboards in indicators above VDI.
3. Wing Sweep ... Bomb (55 deg) (shift-Top Hat down)
4. Jester LANTIRN context menu options:
  1. Head Control
    1. QEyeballs -- A small red circle will appear in the middle of the screen. Look at the target and press the Jester menu key (Comms Hat forward) to ground-stabilize the pod.
    2. Direct Head Control -- A small red dot will appear in the middle of the screen, as well as a small red circle on the VDI display. Put the dot in the circle to "capture" it, then move head to move pod. When on target, press the Jester menu key (Comms Hat forward) to ground-stabilize the pod.
  2. Set Q Mode (LANTIRN cuing options)
    1. QHUD -- Points pod at the center crosshair on HUD. Fly to point the plane at whatever you want, then go to Jester: Ground Stabilize Area or Jester: Next Page -> Designate.
    2. QSNO -- Points pod to centerline of plane, depressed below nose.
    3. QWP -- Points pod at a waypoint.
    4. QDES -- Points pod back to whatever the current designated target is. Useful if Jester loses the target when pod is masked.
    5. QMAP Marker -- Points pod at a map marker, identified by marker label.
  3. Ground Stabilize Area -- Ground-stabilizes the pod but does not automatically designate a target.
  4. Search For Targets -- Tells Jester to begin searching for targets near where the pod is pointing.
    - In the next menu, items marked "(Active)" are for active objects as set in the mission editor, as opposed to static objects. Jester will only automatically search for hostile targets. Most targets except buildings will be "(Active)".
  1. Next Target -- Tells Jester to go to the next target.
  2. Previous Target -- Tells Jester to go to the previous target.
  3. Next Page
    1. Laser Always On -- Turns on the laser and keeps it on, useful for buddy lasing.
    2. Set Laser Code -- Set the code for the LANTIRN laser. The leading "1" is implied, use the options to set the other 3 numbers.
    3. Designate -- Range the target under the crosshairs and designate it as the system target.
    4. Undesignate -- Undesignate the system target.
    5. Disable(Enable) Auto-Designate -- When enabled, Jester will automatically designate a target when he finds one.
    6. Set BHOT(WHOT) -- Toggles black-hot or white-hot display.
    7. Reset -- Resets options on this page to their defaults.
2. Jester should automatically set the LANTIRN laser code to match the bombs, code is shown on the bottom row of the LANTIRN display like "A1688". To have Jester change to a different code:
  1. Jester: Next Page/Utility -> Set Laser Code/Utilty. Current laser code is shown in the center of the Jester menu wheel.
3. By default, Jester should automatically designate any target he finds. If you manually direct the pod, you may need to designate separately with Jester: Next Page/Utility -> Designate.
4. Fly to line up the heading shown at the top of the LANTIRN display.
5. Jester will talk you to the line up and then give you 10 second and 5 second warnings. The line on the right of the LANTIRN display shows the drop cue as a horizontal line moving down to two short horizontal marks.
6. When the line lines up with the marks, press Red Button to drop.
7. Jester will fire the laser when needed.
8. Keep the target on the right side of the plane to give the LANTIRN pod the best view.

Valid laser codes:
Format is ABCC, A=1, B=1-7, C=1-8, never 0 or 9 for any digit. Range should be 1111 to 1788 but may be 1111 to 1688 in the game. A-10C: B=1-6, F-14: B=5-7