1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - ADM-141A TALD

Master Arm ... ON
Master Mode ... A/G

ADM-141A TALD -- Tactical Air-Launched Decoy
Range from 40,000 ft: 68 nmi; from low altitude: 14 nmi
1. Use Jester menu to select Air To Ground Weapons (4), then go through the settings to configure as needed. Current configuration is shown in the center of the Jester menu wheel.
2. Weapon Selector switch ... OFF (Dish Hat down)
3. Selected stations should show checkerboards in indicators above VDI.
4. Fly in the direction you want the decoy to go.
5. Press Red Button to launch.
6. Decoy will pop out its wings and glide as far as it can.