1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Missiles and Guns

Corner speed: 350-420 kts

BVR combat and Radar
1. Press Dish Hat right to enter BVR Master Mode. Radar will automatically turn on. Toggle radar with Pinky Switch up. Radar MFD shows range in top right corner when radar is on.
2. Change range with TDC to top or bottom of screen, or Top Hat Ring.
3. Change elevation with Middle Finger Hat up/down. Radar elevation is shown on left side of MFD, with altitudes of radar cone in 1000x ft. Radar is stabilized in pitch and roll.
4. Toggle azimuth size (60 deg/30 deg) with Middle Finger Hat left/right.
5. In the radar MFD, enemy contacts are a brick, friendly contacts are a circle. Targets are IFF'd automatically.
6. Vertical lines of repeating contacts are jamming you.
7. Press Red Button to fire missiles. Trigger always fires guns.
RWS mode (default):
Cycle PRF modes MED/HI/interleaved with Shift-Middle Finger Hat press.
  - Use MED for targets going away from you or at closer range (<45 km).
  - Use HI for targets coming toward you or at longer range (>45 km).
1. Press TDC Press to lock a target into STT mode.
2. When a target is locked in STT:
  1. Top row of radar screen shows contact TAS, aspect angle, and heading.
  2. Left side of radar screen shows target altitude in thousands of feet ("29-8" = 29,800 ft).
  3. Right side of radar screen shows range to target in nmi and weapon DLZ.
  4. Bottom row of radar screen shows your ground speed, NCTR target ID if available, missile flight time, and target range.
TWS mode and ripple ‌f‌iring AMRAAMs:
1. Toggle RWS/TWS mode with Middle Finger Hat press.
2. Targets show heading with line and altitude in 1000x ft above.
3. To designate first target, move the TDC over the target and lock with TDC Press. Then lock next target (will show as "bugged"), etc. You can designate up to ?? number of targets??.
4. Designate the same target twice in a row to lock it up in STT mode.
5. Firing AMRAAMs will cycle through the targets in turn.

WVR combat and ACM (dogfight) modes
Use Dish Hat for ACM (dogfight) modes:
  - U: Boresight scan
  - D: Vertical scan
  - P: FLOOD mode (guides AIM-7 Sparrow to closest target inside circle on HUD)
1. Press Gray Reset Hat back to toggle gun pipper and auto gun acquisition mode. Trigger is always hot for guns in any mode.
2. ACM dogfight modes automatically lock the first target they see.

AIM-9 Sidewinder variants
Name	Aspect	Smoke	Notes	In service
AIM-9L	All	High		1977
AIM-9M	All	Low		1982
AIM-9P	Rear	High	Improved AIM-9J. Export and USAF use.	1978
AIM-9P3	Rear	Low	Export and USAF use.
AIM-9P5	All	Low	Export and USAF use. Same IRCCM as AIM-9M.

AIM-7 Sparrow variants
Name	Notes	In service
AIM-7E	Base version.	1963
AIM-7F	Improved motor with more range, solid-state guidance system, larger warhead.	1975
AIM-7M	Improved seeker (look-down/shoot-down), fuze, warhead, trajectory guidance.	1982
AIM-7MH	Improved homing algorithm with lofting ability?	1987

AIM-120 AMRAAM variants
Name	Notes	In service
AIM-120B	Improved guidance.	1994
AIM-120C (C-5)	Improved guidance, range, warhead.	2000