1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

300 - Flight - Aircraft Info, Performance Limits

Aircraft Info
- Fuel: Full internal with CFTs: 22,588 lbs
  - Internal only: ~13,100 (58%)
  - CFTs: ~4,750 each, ~9,500 lbs total
  - Droptanks (each): 3,965 lbs
  - Internal with CFTs and 1 droptank: 26,553 lbs
  - Internal with CFTs and 2 droptanks: 30,518 lbs
  - Internal with CFTs and 3 droptanks: 34,483 lbs
  - Ground refueling time: ~2,300 lbs/min avg, 9m50s to fill from empty
    - NOTE Internal fuel (13,100 lbs) fills at 2,600 lbs/min, CFTs fill at 1,900 lbs/min.
lbs	Time	lbs	Time
0	10m02s	12,000	5m25s
1,000	9m39s	13,000	5m02s
2,000	9m16s	14,000	4m31s
3,000	8m53s	15,000	4m00s
4,000	8m30s	16,000	3m28s
5,000	8m07s	17,000	2m56s
6,000	7m43s	18,000	2m25s
7,000	7m20s	19,000	1m53s
8,000	6m57s	20,000	1m22s
9,000	6m34s	21,000	0m50s
10,000	6m11s	22,000	0m19s
11,000	5m48s

- If AOA is above 25 units, speedbrake will not extend.
- Tested max speeds and fuel flows (all testing done with ISA conditions, max fuel, unlimited fuel)
Alt	Mil power					Max power
	KCAS	KTAS	Mach	fuel/eng	fuel tot	KCAS	KTAS	Mach	fuel/eng	fuel tot
Clean, all pylons on, no pods
SL	627	--	0.949	13.4	26.8	732	--	1.107	85.1	170.2
Both pods, 4x Mk 84, 2x gas, 2x AMRAAM, 2x Sidewinder, no center pylon
SL	579	--	0.876	11.8	23.6	683	--	1.034	78.4	156.8
25k	402	563	0.936	7.4	14.8	488	682	1.134	36.4	72.8
30k	352	538	0.912	5.5	11.0	452	669	1.135	29.9	59.8
36k	Can't sustain level flight					401	652	1.133	24.0	48.0

Performance limits
- Landing gear: 250 KCAS (any configuration), 300 KCAS (A/A config without LANTIRN pods)
- Flaps: 250 KCAS
  - Flaps will automatically retract at 250 kts, and re-extend at 230 kts if the flaps switch is down; they will not be damaged by overspeed.
- Tires:
  - Main: 227 kts
  - Nose: 210 kts
- Negative G: 7 sec max
- TFR speed: 370 KCAS/400 kts GS to 0.9 Mach (590 KCAS) to avoid TF algorithm inaccuracies
- Airspeed limits (all with CFTs installed):
  - No LANTIRN pods: 0-36,000 ft: 700 KCAS; 36,000+ ft: Mach 2.0
  - One LANTIRN pod: 0-5,000 ft: Mach 1.0; 5,000-20,000 ft: 625 KCAS; 20,000+ ft: Mach 1.3
  - Two LANTIRN pods: 0-32,000 ft: 700 KCAS; 32,000-48,000 ft: Mach 1.8; 48,000+ ft: decreases with alt up to Mach 1.0 at 70,000 ft

Max Altitudes and Speeds
Drag Indexes
See page in Notes section, 6xx.