1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Autopilot, TFR

Autopilot
- Press A/P button on UFC to turn autopilot on and show the Autopilot menu.
  - Press A/P button again or press Paddle Switch (Brake Lever) to turn the autopilot off.
  - Initial A/P mode (ATT or HDG) depends on current pitch and roll.
- First line of the Autopilot menu shows the current mode: OFF, HDG, ATT, ALT; or one of the "blended" modes: HDG, NAV, GT, CRS, TCN.
- Press L2 OSB to toggle Steer Mode coupling (couples with Steering Mode set on HSI page).
  - NOTE Must be in NAV Master Mode to engage steering coupling??
- Press L3 OSB to toggle Altitude coupling.
  - With Altitude coupling on, press L4 OSB to toggle BARO or RAD altitude.
  - Press R3 OSB to select an altitude to hold, 1,000 to 50,000 ft (or "10" to "50"). Plane will climb or dive, trying to hold constant airspeed to constant Mach as shown next to R4 OSB.

TFR -- WIP
Limits:
  - Min speed: 360 KIAS or 400 KGS, whichever is higher
  - Max speed: 0.97 Mach
  - Roll: 60 deg right, 45 deg left (difference due to pod location under plane), less with increased G
  - FLY UP: If outside the roll limits > 2 secs, or under 75% of the TFR clearance altitude > 2 secs.
1. Set up terrain following clearance height and ride on TF MFD page.
2. Then set switches to activate terrain following:
  1. TF RDR ... ON (left console middle) (T4 switch on throttle base)
    - When ON, TF radar will be transmitting, and symbology will appear on HUD.
  1. Couple to autopilot with TF COUPLE switch on left console forward (T3 switch on throttle base).
    - When coupled, autopilot will handle the altitude, you manually steer with roll. Use A/P page on UFC to enable other AP modes e.g. NAV to follow steerpoints.
  - If Auto Fly Up switch is armed (down), and TF RDR is ON (regardless of TF COUPLE switch setting), FLY UP will happen automatically. If Auto Fly Up switch is disarmed (up), FLY UP will only be automatic if TF COUPLE switch is ON.
TF MFD page shows TFR clearance heights on top OSBs. Allowed heights can change for different modes:
Mode (B1-B5 OSBs; B3 OSB toggles WX1/WX2)	Allowed heights
NORM, ECCM, WX1 (Weather Mode 1)	200, 300, 400, 500, 1000
WX2 (Weather Mode 2), LPI (Low Probability of Intercept)	500, 1000
VLC (Very Low Clearance)	100, 200, 300, 400, 500, 1000

1. Adjust ride with L5 OSB, SOFT or HARD. Max pullup will always be 2 Gs, SOFT gives -0.45 G pushover, HARD gives -0.9 G pushover.
2. Set TFR channel with L3/L4 OSBs to avoid interference with other flight members.
3. E-scope shows a side view of the flight path; you are on the left side of the screen. Range scale (logarithmic) is shown at the bottom. Display symbology:
  - Horizontal line through the middle is your current flight path (velocity vector).
  - Top curved line is Obstacle Warning Line.
  - Bottom curved line is Zero Command Line.
  - Raw radar returns are shown just under the Synthetic terrain line.
  - Command Path?? line should ideally always be between Synthetic Returns and Emergency Pullup line at the top.
1. To recover from FLY UP:
  1. Press and hold Paddle Switch.
  2. Establish flight within all TFR limits (roll, pitch, speed, turn rate).
  3. Release Paddle Switch to resume TFR flight.
TFR emissions from another F-15E can be seen on F-15E's own TEWS. Not sure what effect LPI mode has. TFR emissions seem to be highly directional, and should be short-ranged, but haven't tested much.