1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

305 - Flight - Sequence Points info

General waypoint information
Waypoints are called Sequence Points in the F-15E. There are several types of Sequence Points, the type is determined by the formatting of the Sequence Point number:
Sequence Point type	Format	Notes	Icon
Steer Point	1, 2, 3	Regular navigation point
Aim Point	1.1, 1.2, 2.1, 3.1	Associated with Steer Points. Up to 7 Aim Points for each Steer Point.
Target Point	1., 2., 3. (trailing dot)	When selected in A/G Master Mode, are automatically treated as a target designation.
Offset Point	1.01, 1.02, 2.01, 3.01	Associated with Target Points. Up to 7 Offset Points for each Target Point.
Initial Point	1, 2, 3 (same as Steer Point)	Always the Steer Point immediately before a Target Point.
Aim Point for IP	1.1, 1.2, 2.1, 3.1	Associated with Initial Points. Up to 7 Aim Points for each Initial Point.
Base Point	B	Home base, starting point for INS, common point for all Routes.
Bullseye Point	bullseye icon

- Sequence Points are always assigned to one of three Routes: A, B, or C. Route A is the default. The Route letter will appear after the Sequence Point number, e.g. 1A, 3.01B, etc.
- Each Route has its own set of Sequence Points, and can have the same numbers, e.g. 1A and 1B are two different points.
- There can be a max total of 100 Steering Points and Target Points (combined) across all Routes.
- Note that when entering a Sequence Point on the scratchpad for some other purpose (e.g. to put into UFC as nav point, to put into TPOD or radar as cueing point, etc.) you may need to enter the entire point name (e.g. including the dot). To go to Base Point press SHF then 3 ("B"). You don't have to enter the Route letter unless it's different from the current Route.

Mark Points
- There can be a total of 10 Mark Points, named M1-M10 (select with SHF-5 for M, then number).
- Creating Mark Points:
  - Press MARK button on UFC to create a Mark Point at your current aircraft location.
  - Or change designator action mode on sensor MFD (radar or TGP) to MARK (B2 OSB), then designate to create a Mark Point at the cursor or crosshairs.
    - With TGP, make sure to lase the target first to establish accurate range.
  - Mark Points are always created in order, 1-10, rolling over at the end and overwriting.
- To delete a Mark Point, select the desired point on the UFC (main menu??), then enter 0 on the scratchpad, then press L1 OSB to delete. To delete all Mark Points, enter 0M instead, then press L1 OSB.