1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

307 - Flight - Navigation, Add/Edit Sequence Point, TACAN

Select Sequence Point for navigation
1. Go to main UFC menu (MENU button if not already there)
2. Enter desired Sequence Point on UFC scratchpad, then press R1 OSB (PB 10)

Add/Edit a Sequence Point
IMPORTANT: The currently selected Sequence Point (as shown on the UFC main menu) cannot be edited; select a different Sequence Point first.
1. From main menu on UFC, press R1 OSB (PB 10) to go to Sequence Point menu.
2. Select Sequence Point to edit by entering number on scratchpad and then press L1 OSB, or press L1 OSB with nothing on scratchpad to increment through the Sequence Points in the current route.
  - Create a new Sequence Point by entering a number that is not already assigned as a Sequence Point. It will start with all zeros for lat/long and elevation.
1. Enter point in lat/long DDM format:
  1. Enter Northing on scratchpad: SHF button, then 2 for N or 8 for S, then DDMM.MMM (decimal point optional, will be filled in automatically), then press L2 OSB to enter.
  2. Enter Easting on scratchpad: SHF button, then 4 for W or 6 for E, then DDDMM.MMM (leading zero required; decimal point optional, will be filled in automatically), then press L3 OSB to enter.
  3. Enter altitude in ft on scratchpad, then press R4 OSB to enter.
2. Or enter point in UTM/MGRS format:
  1. Press L4 OSB on UFC to toggle LAT/LONG to UTM mode.
    - Leading grid square designation is shown next to L2 OSB.
    - Elevation is shown next to R4 OSB, and can only be edited on this screen.
  1. Press PROGRAM OSB (R3 OSB) to edit the location.
  2. To change leading grid square designation, press L2 OSB to move ":" cursor to each part of the designation, then press INCR/DECR OSBs (L4/R4 OSBs) to increase/decrease that part.
  3. To change location numbers, enter new grid digits in scratchpad (must be an even number of digits, up to 10), then press L3 OSB to enter.
  4. Press PROGRAM OSB (R3 OSB) to exit editing.
  5. Enter altitude in ft on scratchpad, then press R4 OSB to enter.

Change Steer Point to Target Point (NAV designation) or vice versa
1. On UFC main menu, press R1 OSB to go to Sequence Point menu.
2. Select Sequence Point to edit by entering number on scratchpad and then press L1 OSB, or press L1 OSB with nothing on scratchpad to increment through the Sequence Points in the current route.
3. To change Steer Point to Target Point, enter the Sequence Point number followed by a dot ".", then press L1 OSB to rename the Sequence Point.
4. To change Target Point to Steer Point, enter Sequence Point number with no dot after it, then press L1 OSB to rename the Sequence Point.

Make a Target Point in the Mission Editor
After making a waypoint, set the Name field to "#T".

TACAN navigation
1. On UFC main menu, enter TACAN station on scratchpad, then press L2 OSB to enter.
2. Press L2 OSB again to go to TACAN menu and set options for mode and channel.
3. On HSI page:
  1. TACAN station location and bearing are shown in green.
  2. To get steering information to TACAN, set steering mode to TCN (B1 OSB).
  3. Toggle CDI/PLAN symbology with T1 OSB. CDI gives full Course Deviation Indicator symbology, PLAN gives a simplified view.

Set a Course to a Sequence Point
1. Select Sequence Point you want to navigate to.
2. On HSI page, press B1 OSB to toggle TCN/CRS to CRS.
3. Set desired course with R1 and R2 OSBs, or enter course on scratchpad and press either R1 or R2 OSBs.
4. Toggle CDI/PLAN symbology with T1 OSB. CDI gives full Course Deviation Indicator symbology, PLAN gives a simplified view.