1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A2A - Radar display and settings

Radar display and settings
- Upper left text shows BRA (bearing on top, range below) to TDC cursor (aka "ack symbols", "| |")
- Top line of text shows locked target's speed, aspect, and heading.
- Bottom left text shows bullseye bearing/range to TDC cursor
- Bottom line of text shows ownship ground speed on left, airspeed on right.
- May have to change channel letter/number to deconflict radar freqs. (T1 and T2 OSBs) One flight would typically be one one letter, with flight members on different numbers.
- Number on the right of the TDC cursor are top and bottom altitudes of radar scan at the TDC cursor distance.
- Number on left side of TDC cursor when hovering over a target shows target's altitude.
- Targets are shown as a solid square or triangle. Square means low closure rate, triangle pointing down means coming toward you, pointing up means going away from you.
- TWS doesn't track targets through the notch as well as STT does.
- Caret at top of scope indicates targets that are beyond currently shown range.
- Hollow triangles are steerpoints.
- Typical config:
  - Long range scan: 4-bar, 120 deg, INLV, FS 1, GMTR CHAF
  - Shorter range scan: 6-bar, 60 deg, INVL, FS 1, GMTR CHAF
- Settings:
Name	OSB	Values	Function
EL (Bars)	L2	1, 2, 4, 6, or 8	Total elevation range of radar
FS	L3	0, 1, 2	Frame Store -- Number of full scans after which a contact will be cleared if not detected again.
GMTR	L4	LO, MED, HI, CHAF	Ground Moving Target Rejection / LO - 45 kts, may show false targets or ground targets / MED - 63 kts / HI - 87 kts / CHAF - 95 kts, may eliminate helicopters or slow targets
PRF	B1	HI, MED, INLV	HI PRF -- long range, large targets, closing targets / MED PRF -- shorter range (80 nmi max), smaller targets, low altitude targets, chasing targets
RGH	B2	on/off	Range Gate High -- Special PRF mode between MED and HI. Rarely used??
VCTR	B3	on/off	Vector search -- Very slow search mode for small RCS targets or very long range.
ENTER	B5	--	Saves current radar settings to MRM or SRM mode (whichever is selected) as its new default.