1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A2G - Radar HRM

Making HRM patch maps
HRM patch map sizes and ranges
Map size	Max range
80	160 nmi
40	160 nmi
20	160 nmi
10	160 nmi
4.7	80 nmi
3.3	50 nmi
1.3	40 nmi
.67	40 nmi

- Grazing angles:
  - Best grazing angle is 2-10 degrees down from the nose, minimum usable angle is 0.5 degrees down from the nose, max is 20 degrees down.
  - Rule of thumb: For a 1 deg grazing angle, be at 1000 ft altitude per 10 nmi distance.
  - Map accuracy is better toward the edges of the gimbal, +/- 60 deg.
  - Formulas
    - tan(90 - grazingAngle) = range / alt
    - alt = (rangeNmi * 6076.12) / tan(90 - grazingAngle)
    - range = tan(90 - grazingAngle) * alt
- Grazing angle altitude/range table:
Range / (nmi)	Altitude (ft) for grazing angle					Notes
	-0.5°	-1°	-2°	-10°	-20°	Alt is ft above target
5	265	530	1,061	5,357	11,058
10	530	1,061	2,122	10,714	22,115
15	795	1,591	3,183	16,071	33,173
20	1,061	2,121	4,244	21,428	44,231
25	1,326	2,651	5,305	26,785	55,288
30	1,591	3,182	6,365	32,142	66,346
35	1,856	3,712	7,426	37,498	77,403
40	2,121	4,242	8,487	42,855	88,461	max 0.67 HRM range
45	2,386	4,773	9,548	48,212	99,519
50	2,651	5,303	10,609	53,569	110,576	max 3.3 HRM range
55	2,916	5,833	11,670	58,926	121,634
60	3,182	6,364	12,731	64,283	132,692
65	3,447	6,894	13,792	69,640	143,749
70	3,712	7,424	14,853	74,997	154,807
75	3,977	7,954	15,914	80,354	165,865
80	4,242	8,485	16,975	85,711	176,922	max 4.7+ HRM range

General flow for HRM -- Front Seat
1. Go to A/G radar page, take command, and set to RBM mode initially (B1 OSB).
2. Set the cursor function to MAP (B2 OSB).
3. Find target area. Jump cursor directly to a Sequence Point by entering SP number on scratchpad and pressing T4 OSB.
4. Use Gray Reset Hat forward/aft to change the HRM map size.
5. FREEZE mode -- At any time, either in RBM mode or with a HRM map, press Pinky Button to toggle FREEZE. The current scan or map will finish, and then radar will deactivate. Press TDC press again to do a new map, or toggle freeze mode off to resume continuous mapping.
6. Press TDC press to begin mapping.
7. HRM page settings:
  1. Press L3 OSB to toggle ML1/ML2. ML2 gives better map quality, takes 1.5x longer.
  2. Press L2 OSB to toggle STB/progressive?? STB (stabilized) means continuous re-maps will be on the same ground location, progressive means new map location will move with the plane.
  3. Press R2 OSB to go to HRM PPI mode, which clears the current map and returns to a large-scale HRM similar to RBM. Note grazing angles make it not very useful at low altitude.
  4. Press R1 OSB to store the current map (only possible when in FREEZE mode). Press B5 OSB to toggle NEW/OLD, to show current and previous map image. New maps will always overwrite the map currently being displayed and the current map will become the OLD map.
8. When you have a map of the target, change cursor mode to TGT (B2 OSB). Press TDC press to designate a target on the map.
  - In HRM, recommended to designate small targets (e.g. vehicles) on bottom edge of radar return. Due to radar physics, this will correspond more closely with the actual center of the target.