1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A2G - Radar PVU

PVU -- Precision Velocity Update -- WIP
Should only be needed pre-GPS (1996 or earlier??)
1. Go to A/G RDR page, take command, set to PVU mode (B1 OSB).
2. Select type of update:
  - MN OSB (B3 OSB)-- Mission Navigator, a quick, short-term update that only affects the radar, not the INS. Takes about 10 seconds, lasts 5 minutes before being automatically cleared.
  - INS OSB (B4 OSB) -- A longer update that affects the entire INS. Takes 3-6 minutes, requires maneuvering.
  - IPVU / MN OSB (T5 OSB) -- Toggles Interleaved PVU, radar enters PVU mode once per minute and does an auto-update, not as good as manual PVU modes, but can be toggled and used in any A/G radar mode.
Controls:
  - LAN / SEA OSB (L2 OSB) -- Toggles land or sea mode. Sea mode is less accurate, but works over water.
  - RST OSB (L4 OSB) -- Resets the current update data and starts updating from scratch.
  - CLR OSB (L5 OSB) -- Clears the MN update and restores nav system to state it was in before MN update. This is done automatically 5 minutes after doing an MN update.
1. MN update:
  1. Press TDC press to begin updating. Screen will say UPDATE.
  2. UPDATE will disappear after about 5 seconds, and the update is complete.
2. INS update: -- WIP
  1. Press TDC press to begin updating. Screen will say UPDATE.
  2. UPDATE will disappear after about 5 seconds, but update process will continue until you press TDC press again??
  3. Recommended to update for 3-6 minutes, with 90-180 deg heading changes, climbs, dives, acceleration, and deceleration.