1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A2G - Designating targets

NAV designation -- Turn a Sequence Point (waypoint) into a Target Point
1. On UFC, go to MENU 1
2. Press R1 OSB (PB 10) to enter Steer Point menu.
3. Enter desired Sequence Point and add a dot "." after it, then press R1 OSB again to rename the sequence point.
  - Note: Can only do this on a Sequence Point that is not your currently selected navigation point (as shown on UFC main menu).

Radar designation
1. On A/G radar page, take command of the radar.
2. Select desired radar mode (RBM, GMT, or HRM) and find the target.
3. Set cursor function to TGT (B2 OSB, PB 07).
4. Put TDC cursor on target and press TDC press to designate.
  - In HRM, recommended to designate small targets (e.g. vehicles) on bottom edge of radar return. Due to radar physics, this will correspond more closely with the actual center of the target.

HUD designation -- WIP
1. SOI to HUD: Press Dish Hat press, then Dish Hat up??
2. HUD pipper
  1. Press and hold TDC ministick to slew designator diamond, release to set point.
  2. Press and release TDC ministick to designate at velocity vector??
3. CDIP designation
  1. If in CDIP mode, designation will be automatically updated to weapon impact point when pickle is pressed?? If CDIP point would be off bottom of HUD, press and hold pickle to designate target and switch to automatic CCRP mode until bombs drop.

TPOD designation
1. On TPOD page, take command of the TPOD.
2. Slew TPOD to target.
3. Set cursor function to TGT (B2 OSB, PB 07).
4. Press TDC press to designate.
5. (optional) Box CDES OSB to continually update designation point as TPOD slews.