1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

506 - A2G - Unguided Bombs

Fence in
- A/G Master Mode
- Master Arm ON

Bomb setup
- All bombs, on ARMT > A/G page:
  - CDIP, AUTO ... CCIP/CCRP mode
  - 1/STA, STEP ... One bomb from each selected station, or one bomb only, alternating stations.
  - RP SGL, RP MULT ... While pickle is held, drops up to QTY bombs, at INTVL ft spacing, alternating stations, or from each selected station.
  - NOSE, TAIL, N/T ... For Mk 82 Snakeye, Mk 82 AIR, and Mk 84 AIR, TAIL or N/T enables high-drag fins/parachute, NOSE disables the high-drag and drops them as slicks.
  - BOT ... Determines which bomb in the string will fall on the target. CTR (default) is center bomb, press to cycle bomb number, or enter on scratchpad.
- CBU-87/-97 special fuzing options
  - On ARMT > A/G LOAD page, when loading CBU-87/-97, press FUZE OSB to set burst time, burst height, and spin. Burst time and height are shown on the page, spin numbers are as follows:
SPIN n:	1	2	3	4	5	6
RPM:	0	500	1000	1500	2000	2500

- A/G DLVRY page -- WIP
  - PROG PAGE
    - LOFT ... Set loft angle (cues for auto loft bombing)
    - AT ... Along Track bias, positive numbers move impact point long, negative numbers move impact point short (in ft??).
    - CT ... Cross Track bias, positive for right, negative for left.
    - TARM ... Time to Arm, arm time after dropping, in seconds.

CDIP (CCIP) bombing
1. Set up bombs, see settings above.
2. To use radar AGR for slant range, put HUD in CMD with Dish Hat press then Dish Hat up. HUD should say IN CMD on left side, and AGR should appear on right side.
3. Put pipper on target, press and hold Red Button to drop.
4. If pipper would be off bottom of HUD, press and hold Red Button to designate target and enter auto CCRP mode until drop.
Mk 82, Mk 84
CCIP is accurate in a dive of about 15 deg and greater. Less accurate in shallower dive or level flight.
Mk 20 Rockeye
- Use TIME mode rather than HEIGHT; Mk 20 doesn't have a radar altimeter.
- CCIP is accurate for both dive and level releases, including low altitude level bombing. No longer accurate as of 2024-02-24 patch.

AUTO (CCRP) bombing
1. Set up bombs, see settings above.
2. Designate target.
3. Fly toward bomb fall line (ASL). HUD shows time to release (TREL).
4. When release cue (short horizontal line) starts coming down the bomb fall line, press and hold Red Button until release cue hits velocity vector and all bombs drop.
Toss bombing
Manual loft:
  - In a low alt (~200 ft AGL), high speed attack (~0.85 Mach):
  1. When 20 seconds away from target (~3.5 nmi), hold pickle and initiate pull up to about 20-25 deg nose up, then stop pulling and stabilize in a steady climb. Watch for release cue line coming down the bomb fall line.
Auto loft:
  1. Go to ARMT > A/G > A/G DLVRY > PROG PAGE.
  2. Enter desired loft angle on scratchpad, then press LOFT OSB (L2 OSB) to set.
    1. Recommend 40 deg?? for best distance, or 25 deg for lower max exposure height.
  3. HUD will show time to loft pullup as TPULL.
  4. 5 seconds before TPULL, HUD will show pullup cue: a long horizontal line.
  5. Press and hold pickle. When TPULL hits 0, pull up at around 4G, keeping the velocity vector on the pullup cue line and centered on the bomb fall line.
  6. Release cue is a shorter horizontal line that comes down the bomb fall line. When the release cue reaches the velocity vector, bombs are released. Keep the pickle down until they're all gone.

Weapon notes
- Mk-84 AIR can be dropped safely from as low as 160 ft and 0.500 Mach.
- More TODO...