1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507 - A2G - Laser Guided Bombs

Fence in
- A/G Master Mode
- Master Arm ON

Bug: If GBU-10s (and/or maybe GBU-12s) are carried only on one CFT, they should be carried only on the right CFT, not the left. CCRP bomb fall line may be stuck on extreme left or right otherwise.

Laser guided bombs
Bomb setup:
  - On ARMT -> A/G page:
  - AUTO	CCRP mode
  - STEP	One bomb only will be dropped per pickle, alternating stations if multiple stations are selected.
  - FUZING	As desired
1. Designate target
2. Go to TPOD page and take command.
3. Set laser code by entering in scratchpad and pressing T2 OSB (PB 19).
4. Toggle Auto/Manual lasing with T3 OSB (PB 18).
  - To set ALAS time, go to ARMT -> A/G -> PROG PAGE, B3 OSB.
1. Fly toward bomb fall line (ASL).
2. HUD shows time to release (TREL).
3. When release cue starts coming down the ASL, press and hold pickle until release cue hits velocity vector and all bombs drop.
4. If using Manual lasing, press Pinky Button (with TPOD IN CMD) to toggle laser.

GBU toss/loft attack
- LANTIRN pod has a max side look of 135 deg left (maybe less to the right??).
- In a low alt (~200 ft AGL), high speed attack (~0.85 Mach):
Set heading bug (HDG OSB on HSI page) 60 deg left or right of inbound heading, right preferred.
  - Absolute max egress heading seems to be about 70 degs off attack heading, but that's very marginal and may mask the pod right before impact.
1. Recommended to put HSI page on one of the MFDs. Heading bug appears on HSI page, and in bottom right of HUD as a number only (no indicator in heading tape).
2. When 20 seconds away from target (~3.5 nmi), hold pickle and initiate pull up to about 20-25 deg nose up, then stop pulling and stabilize in a steady climb. Watch for release cue line coming down the bomb fall line.
3. On release, immediately pull hard up and over to partly inverted toward egress heading.
4. When on egress heading, roll upright and begin shallow dive (~5 deg).
5. Bomb should impact just before target goes out of FOV.
  - If target goes out of FOV, you can get a few extra seconds by going full rudder toward the target.
Release should happen around 1000 ft AGL, your max alt should be about 2800 ft, closest approach to target about 2.4 nmi, total exposure time should be about 30 seconds.

Back seat flow -- WIP
- If TPOD on left side:
  - Press Middle Finger Hat right to take command of Left MPD (TPOD).
  - On TPOD page, set cursor mode to TGT.
  - Use TDC ministick to slew.
  - Press Rear Thumb Button ("Trigger full-action") to designate.
  - Press Lower Thumb Hat press to toggle tracking on/off (ATRK or PTRK).
  - Press Lower Thumb Hat forward short to cycle zoom.
  - Press Pinky Button press to toggle laser on/off.
- If TPOD on right side:
  - Press shift-Dish Hat left to take command of Right MPD (TPOD).
  - On TPOD page, set cursor mode to TGT.
  - Use Dish Hat to slew.
  - Press Trigger Stage 2 ("Trigger full-action") to designate.
  - Press Gray Reset Hat press to toggle tracking on/off (ATRK or PTRK).
  - Press Gray Reset Hat forward short to cycle zoom.
  - Press Lower Gray Button to toggle laser on/off.