1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

508 - A2G - JDAMs

Fence in
- A/G Master Mode
- Master Arm ON

JDAMs with target from TPOD, RDR, NAV, or HUD -- WIP
Bomb setup:
  - NOTE: JDAMs self-identify to the ARMT page when loaded.
  1. On ARMT -> A/G page:
    1. DIRECT / STEP / N/T recommended.
      - DIRECT recommended because it allows pickling any time, while AUTO will only pickle at a specific spot (partway inside IN ZONE, shown by tick mark in range scale on HUD).
      - STEP recommended because RPL SGL is currently bugged or not working correctly.
  1. Then open SMRT WPNS page (in M2 menu page):
    1. Select the program number you set up on the A/G page.
2. Designate target with TPOD, RDR, TGT steerpoint, or whatever.
3. Press XFR xxx OSB (L1 OSB) (xxx will be SEQ PT, RDR, TPOD, or HUD depending on what you're targeting with).
  1. Coordinates should populate after a moment.
  2. Optional: Press NXT STA OSB (PB 02) to cycle to the next bomb in the program, designate, press XFR xxx again, repeat until all bombs have a target assigned to them.
  - NOTE: For SEQ PT designation (from a targetpoint), nothing else should be designated; you may have to undesignate your radar or tpod target (Boat Switch aft (Rear Thumb button)).
When IN RANGE (in LAR) shows on HUD, you will get ASL line. Can drop there or wait until IN ZONE. If IN RANGE only, bomb will not be able to meet terminal parameters (velocity, heading, impact angle) but should still hit (needs testing).

JDAMs with manually entered coordinates
1. Set up bombs as above, and go to the SMRT WPNS page.
2. Press EDIT MSN OSB (R2 OSB).
3. Use up/down/left/right arrow OSBs (L4-L5 and B1-B2) to move data entry box around the screen.
4. Enter northing and easting coordinates in UFC when the data entry box is on the appropriate spot (TGT section on left lower). Format is DDM: DDMMmmm
5. Press EDIT OSB to pass the data from UFC to the data entry box, or to cycle through options.
6. Press XFER xxx OSB (B4 OSB) to cycle through WPN, PROG, or ALL. When you transfer the data, this controls what it will be transferred to: WPN = selected weapon only, PROG = every weapon selected for this PROG, ALL = every weapon on the plane.
7. When finished, press MSN XFER (B5 OSB) to save target coords to the selected XFER destination (as set on B4 OSB).

JDAMs with target predefined in Mission Editor
TODO...

LJDAMs -- WIP
1. Follow steps above to set up bombs like regular JDAMs.
2. If dropped with no lasing, they will act just like normal JDAMs. However if they see a laser dot, they will update their coordinates to the laser dot as long as the dot is visible. If the dot goes away, they will guide to the last place it was seen.
3. To set bomb's laser code, press SENSOR OSB (T1 OSB) when weapon is selected on SMRT WPNS page.
4. Then enter new laser code into UFC and press LASE OSB (T2 OSB) to set. Then go back to SMRT WPNS page.
5. NOTE: If set to ALAS (default), laser will automatically fire when dropping an LJDAM; if you don't want it to guide on the laser, toggle laser to manual lasing (MLAS) with TPOD T3 OSB or SAFE with TPOD T2 OSB.
6. If using Manual lasing, press Pinky Button (with TPOD IN CMD) to toggle laser.

JDAM toss/loft attack
In a low alt (~200 ft AGL), high speed attack (~0.85 Mach):
1. Initiate pullup at about 5.5 nmi from the target.
  1. Notso tutorial video says begin pullup for 10 deg loft at 7.0 miles, 30 deg loft at 10.0 miles... test??
2. Pull to 20-25 deg nose up and pickle.
  - Up to at least 35 deg works OK, but increases exposure time and doesn't increase the max range.
1. Keep pulling around an over inverted away from target and get back down low.
2. Release should happen around 1,500 ft AGL, your max alt should be about 2,500-3,000 ft, closest distance to target should be about 4.3 nmi, total exposure time should be under 20 secs.

Back seat flow -- TODO
TODO