1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507b - A/G - AGM-88C HARMs with HTS pod -- WIP

Master Arm ... ON
Master Mode ... A/G
Left cheek pylon power ... ON (for the HTS pod)
SMS page ... Select AG88 and PWR ON

(HARMs can be carried on stations 3, 4, 6, and 7, but in USAF service are only carried on stations 3 and 7.)

HTS/HAD - HARM Targeting System pod/HARM Attack Display
1. On left MFD, go to menu, HAD OSB (T2). Emitters will be detected and shown as colored squares.
2. Set SOI to HAD page (Dish Hat down to toggle SOI).
3. Move cursor over emitter to show location data, press TMS up to lock emitter and hand-off to HARM.
  - Locking an emitter creates a SPI and can be used to cue other sensors such as TPOD as well.
  - Press TMS left to show target data on DED display, TMS right to cycle through emitters on HAD page, TMS down to unlock.
  - Top of HAD shows bearing, distance error, lateral error, arming status, position quality (PGM). PGM1 is best position quality, PGM5 is worst.
  - White box means it's locked, red inside the white box means a HARM has been handed off to it.
  - Bottom right corner shows time to impact, time at impact, and HARM targeting mode (PB/EOM/RUK)
  - Emitter colors:
    - Yellow -- Default color for emitters.
    - Red steady -- Emitter is in Track mode.
    - Red flashing -- Emitter is in Launch mode.
    - Green -- No emissions detected for at least 2 minutes.
    - If no emissions are detected for over 4 minutes, the emitter is removed from the display.
1. HARM WEZ (Weapon Engagement Zone) is shown with white lobed outline on HAD screen. WEZ changes with your speed, altitude, and attitude.
2. When location is sufficiently known (PGM1 or PGM2) and within launch parameters/DLZ, press Red Button to fire missile.
- Targeting an emitter on the HTS also automatically sets the SPI; you can switch to the TGP and it should be pointed at the target automatically.
- HTS refines the position over time; for best results, fly perpendicular to the emitters to allow a longer triangulation leg.
- HTS searches for up to 11 "Classes" of emitters (groups of emitters, like tables), plus another class of up to 8 manually-specified emitters.
- HARM mode (PB/EOM/RUK) affects the footprint size and launch area on the HAD. Speed and altitude also affects the footprint.

To set the HTS search classes (affects search refresh rate):
1. On HAD page, press THRT OSB (T4).
2. CLASSes that are highlighted in white are active. Press corresponding OSBs to toggle active classes and speed up the refresh rate. Refresh rate is shown near top of OSB as SCT X:XX (minutes:seconds).
3. To use the manually-specified class:
  1. LIST button on UFC.
  2. 0 for MISC.
  3. ENTR ("E") for HTS.
  4. Select field with Dobber up/down.
  5. Type new ID on UFC keypad, then press ENTR.
  6. As soon as one is entered, HAD/THRT page will show a new MAN OSB (T2) at the top. Press MAN OSB to highlight it in white and add your emitters to the search. Other Classes can be disabled if desired to greatly speed up the refresh rate.
  7. When finished, press RTN on Dobber switch to return to main DED page.

HTS with datalink -- WIP, needs verification
- Needs at least 3 F-16s with HTS as Team Members, with TDOA box checked in Mission Editor.
  - TODO: Is TDOA behavior on by default if you add a new Team Member in flight? TDOA status is shown on datalink page on DED, the one that lists members and that you can edit, it's the T column in front of the STN.
1. Set HAD page as SOI.
2. Set emitter as SPI on HAD page (slew cursor, then TMS up (Gray Reset Hat forward)).
3. Make sure your Team Members do not have an emitter designated on their HADs.
4. Send your emitter designation to Team Members with Middle Finger Hat right long.
5. Your HUD will say TDOA.
  1. TODO: How to clear?? WARN/RESET switch??
6. Other Team Members will then designate that emitter automatically and begin sending you data.
  1. Your HAD page should show "TD-M" at bottom left, meaning you are the Master for this target.
  2. Other Members' HAD page should show "TD-S" at bottom left, meaning they are the Slaves.
7. Position Quality (PGMn) for you should quickly improve. PGM for Team Members will only be as good as their individual planes (datalink only goes from Slaves to Master, not back down).