1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

300 - Flight - Aircraft Info, Performance Limits

Aircraft Info
Fuel:
Config	External fuel	Total fuel
Internal only	0 lbs	12,149 lbs
Wing tanks (2,470 lbs each)	4,940 lbs	17,089 lbs
Centerline tank (4,005 lbs)	4,005 lbs	16,154 lbs
Wing+Centerline	8,945 lbs	21,094 lbs

- Ground refueling time: ~1,735 lbs/min avg, 7m19s to fill from empty
  - NOTE Fuselage tanks (~8,800 lbs, 72%) fill at ~2,650 lbs/min, wing tanks (~4,200 lbs) fill at ~830 lbs/min.
lbs	Time
0	7m19s
1,000	6m56s
2,000	6m33s
3,000	6m11s
4,000	5m48s
5,000	5m25s
6,000	5m03s
7,000	4m40s
8,000	4m17s
9,000	3m45s
10,000	2m33s
11,000	1m22s
12,000	0m11s

- Best sustained turn rate??:
  - Sea level: 0.78 Mach/525 KIAS, 14.75 deg/sec (4x AIM-7 only), 14.10 deg/sec (4x AIM-7 + 4x AIM-9)
  - 35,000 ft: 0.85 Mach/300 KIAS, 4.5 deg/sec (4x AIM-7 only), 4.0 deg/sec (4x AIM-7 + 4x AIM-9)

Performance Limits
- Landing gear: 250 KIAS
- Flaps: 250 KIAS
- Slats: 600 KIAS or 2.0 Mach
- Air refueling door: 320 KIAS (open/closing), 400 KIAS (static)
- Canopy open: 60 KIAS
- Drag chute deployment: 200 KIAS
- Cockpit access steps extended: 400 KIAS
- APU: 600 KIAS or 0.95 Mach
- AOA:
  - On Speed: 18.7-19.6 units
  - Max: 30 units below 35,000 ft, 25 units above 35,000 ft
  - Max performance turn: 25 units while subsonic
- Negative G: 30 sec
- Zero G: 10 sec
- Airframe max speeds:
  - Max speed in level flight attained at 36,000 ft, Mach 2.04.
  - Below 30,000 ft: 750 KIAS
  - 30,000 ft to 45,000 ft: 700 KIAS
  - Above 45,000 ft: 2.0 Mach (normal limit), 2.4 Mach (transient limit)
  - Between 650 KIAS and 750 KIAS, above 10,000 ft, when going from AB to Mil power, move throttles slowly and allow the plane to decelerate, otherwise could damage exhaust nozzles.
- Max Gs:
  - Absolute max: 8.5 Gs subsonic, 6.5 Gs supersonic
  - Asymmetric loads and specific stores may have lower limits.