1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Climb, Cruise, Landing, Spin Recovery

Takeoff
1. Canopy ... Close (normal to taxi with canopy open)
2. Slats out, flaps down.
3. Brakes should hold 85% power.
4. Use NWS or rudder for directional control, do not use differential braking.
5. At 80 kts, hold stick full back until rotation, then ease to about half back and maintain 10-12 deg pitch.
  1. Rotate speed should be around 120-140 kts (light to heavy gross weight, aft CG up to 15 kts slower, forward CG up to 15 kts faster).
6. Gear and flaps up before 250 kts.
7. If carrying external tanks: EXT TANKS switch ... OUTBD for wing tanks or CENTER for centerline tank (triangle-shaped switch, left console rear outboard)

Climb
Maintain 10-12 deg pitch until 350 kts, then maintain 350 kts until Mach 0.9, then maintain Mach 0.9 until desired altitude.

Cruise -- Optimum speeds and altitudes
Drag Index ->	0	70	140
Gross Weight
30,000	0.875 Mach, 44,000 ft	0.820 Mach, 43,000 ft	0.680 Mach, 36,000 ft
45,000	0.875 Mach, 37,000 ft	0.820 Mach, 34,000 ft	0.680 Mach, 27,000 ft
60,000	0.875 Mach, 31,000 ft	0.820 Mach, 27,000 ft	0.680 Mach, 20,000 ft

Landing
1. Below 250 kts, gear down, slats out, flaps down. Flaps may not actually come down until 210 kts.
2. 180 kts minimum on downwind leg.
3. Maintain 19.2 AOA on approach. For high crosswinds or high internal fuel loads (aft CG), or no slats, use 17.0 AOA.
4. Onspeed AOA is 18.7 to 19.6 units (avg 19.15). AOA indexer symbols:
  1. ⋁ ... AOA too high, speed up
  2. O ... On speed
  3. ⋀ ... AOA too low, slow down
5. Flare optional. Drag chute optional.
6. For max braking, pull full aft stick during landing roll and maximum brakes.
7. If you need to go around, accelerate to 180 kts minimum before retracting slats and flaps. Avoid using AB unless necessary.

Spin recovery
1. Stick full forward and hold, ailerons and rudder neutral, throttles idle.
2. If no recovery, deploy drag chute.
3. Roll in direction of spin, maintain full forward stick.
4. When G forces go negative, ailerons neutral.
5. Maintain full forward stick until roll and yaw stops, then neutralize controls.
6. Maintain 3-8 units AOA until over stall speed.
7. Drag chute will fail at about 250 kts or can be jettisoned.
8. Begin pulling up, don't exceed 25 units AOA, throttles as needed.
9. If still out of control at 10,000 ft above terrain, eject.