1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Radios

Radio setup and tuning -- Pilot and WSO
Band	Frequency range	Modulation	T/R	Notes
COM1 -- ASQ-19
VHF/UHF	225.000 to 399.975 MHz	AM	T/R	"COMM"
VHF/UHF	265.000 to 284.900 MHz	AM	R	"AUX"

General info
- Pilot radio (COMM PANEL) is on right console forward inboard, WSO radio is on left console rear inboard.
- COMM CMD button (small black button on far forward left of panel) toggles between Pilot and WSO radios. Either Pilot or WSO can toggle. If COMM CMD light is lit in your cockpit, your radio is active for both cockpits.
Using preset frequencies:
1. Frequency Mode switch ... PRESET
2. COMM CHAN knob ... turn to desired channel (1-18)
Preset frequencies cannot be changed, they're set in the Mission Editor. A list of channels and frequencies is in the built-in kneeboard pages.
Using manual frequencies:
1. Frequency Mode switch ... MANUAL
2. Frequency knobs ... tune to desired frequency (if you can't turn a knob, check that you're not trying to tune an invalid frequency)

Possible bug? Can't figure out how to make Jester set a manual frequency. You can enter the frequency in the Jester menu, but don't know how to make Jester actually set it. In the meantime, you can just go to the back seat and set up the radio yourself.