1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Navigation, Autopilot

Waypoints using Navigation Computer -- AN/ASN-46A -- WIP
- Navigation computer controls are on WSO right console
- Supports 2 waypoints: TGT1 and TGT2.
1. Set TGT1 location:
  1. TODO...
2. Set TGT2 location:
  1. TODO...
3. Switch from TGT1 to TGT2:
  1. TODO...

In-flight inertial navigation fix update
TODO

TACAN navigation -- WIP
1. TACAN controls are in both cockpits, right console.
2. Max TACAN range is 390 miles for ground stations, 200 miles for air stations.
3. Press NAV CMD button to take command in that cockpit. Green light next to button illuminates if you have command.
4. Tune TACAN reciever:
  1. Jester: Navigation > TACAN > Tune Tac > (select TACAN unit)
  2. Or in pilot seat, set channel, X/Y, and mode, then press NAV CMD button to take command.
  3. To receive A/A TACAN, receiver channel must be set to 63 channels above or below transmitting channel, and same X or Y.
5. Display Mode button ... CRUISE (Mode dial 2)
6. STEER CMD buttons ... TACAN (right console bottom)
7. HSD shows a triangle on the outside of the compass wheel indicating direction to TACAN station, "+" is the reciprocal. Top left shows range to TACAN station.
8. HSI compass to right of VDI also shows arrow pointing to TACAN and range in window.

VOR navigation
TODO

Waypoints from F10 map using Jester -- WIP needs verification
1. Add marker to the F10 map, name it whatever you want.
2. Jester menu -> Navigation?? -> Map Markers -> select marker by name

AFCS (autopilot) and Stab Aug
- To turn on AFCS, at least the PITCH stab aug must be on, but YAW and ROLL are needed as well for full functionality.
- Toggle AFCS switch with shift-Trim Hat up. This engages attitude/heading hold.
- While AFCS engaged, toggle altitude hold with shift-Trim Hat down.
- AFCS functionality:
  - If within 5 deg of wings-level, holds heading with wings level.
  - If rolled more than 5 deg, holds bank angle.
  - Pitch angle is always held, unless altitude hold switch is on.
  - Press Flip-down Trigger (NWS button) to toggle heading or attitude hold.
  - You can override the AFCS with light stick pressure in any direction.
- Pull and hold the brake lever to disable AFCS, all Stab Aug channels, anti-skid, and aileron-rudder interconnect (ARI). When brake lever is released, AFCS will remain disabled, but all others will revert to their current switch settings.
- IMPORTANT Do not attempt to fly the aircraft from the WSO seat when AFCS is engaged. It'll mess up the trim and may cause violent control movements when AFCS is disengaged.