1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Radar Modes

WSO seat:
AHC = Antenna Hand Control. Joystick on right console used to control radar antenna.

ASPECT knob
With locked target, ASPECT knob shows different information in the top-right readout in radar screen:
ASPECT knob setting	Shows	Units
WIDE	Target Vc (closure velocity)	Kts, positive is closing, negative is opening
NOSE	Target Altitude	Hundreds of ft, so "200" is 20,000 ft
FWD	Target Aspect	0 is flying directly away, 180 is flying directly towards, negative is left, positive is right
AFT	Target Vc (closure velocity)	Kts, positive is closing, negative is opening
TAIL	Target Heading	Degrees from 000 to 360, last number will always be 0

Sensitivity Time Control
Radar returns get dimmer at longer distances. When radar MODE knob is in MAP and DISPLAY knob is in PPI WIDE or PPI NAR, distant returns will automatically get amplified proportionally to provide an even brightness at all ranges.

radar controls

POWER knob
- 5 position: OFF, TEST, STBY, OPR, EMER
- Normal position: OPR
- Warmup takes 3 minutes, starts when you go from OFF to TEST or STBY.
- Should only need STBY and OPR settings.
POLAR switch
- 3 position: LIN, CIR1, CIR2
- Normal position: LIN (linear vertical polarization).
- CIR 1 and CIR 2 can be used to reduce rain/cloud clutter, but will increase ground clutter. Sparrows can only be guided with LIN and CIR 1, not CIR 2.
RANGE knob
- 6 position: 5, 10, 25, 50, 100, 200
- Normal position: 5 to 50 ("AI" ranges)
- Automatic Tracking (target lock) only available up to 50 nmi.
- 100 and 200 nmi ranges can be used for Spotlight technique to manually monitor a target.
MANEUVER switch
- 2 position: HI G, LOW G
- Normal position: LOW G??
- LOW G reduces automatic tracking acceleration to reduce sensitivity to countermeasures and clutter.
- HI G allows unlimited tracking acceleration.
SCAN switch
- 2 position: 1 BAR, 2 BAR
- Normal position: 1 BAR
- 1 BAR covers 6.7 deg with nutation, 3.7 degrees without nutation.
- 2 BAR covers 10.45 degrees, scan alternates between 1.875 deg above/below radar plane.
- Only used when radar MODE knob is set to RDR??
ASPECT knob
- 5 position: WIDE, NOSE, FWD, AFT, TAIL
- Normal position: WIDE, but frequently changed??
- When shooting Sparrows with no lock, provides a speed gate for the Sparrow to guide.
- When radar is locked on a target, changes the top-right readout on the radar screen to various target data (closure, altitude, aspect, closure, heading, respectively)
RCVR GAIN knob
- 2 analog knobs: COARSE (outer/bottom/larger knob), FINE (inner/top/smaller knob)
- Controls radar gain. Normally should be adjusted up until small amount of noise is showing.
- When locked on a target, gain becomes automatic, and knob settings are ignored while locked.
TRACK switch
- 3 position: MAN, AUTO, AOJ OUT
- Normal position: AUTO
- AOJ OUT disables automatic Home On Jam if jamming is detected erroneously.
- MAN uses the velocity setting from the MAN Vc knob to set the tracking gate closure velocity.
DISPLAY knob
- 5 position: VI, B NAR, B WIDE, PPI WIDE, PPI NAR
- In B-scope modes, vertical lines are constant azimuth, so bottom of scope looks "spread out".
- In PPI modes, real position of targets in relation to aircraft are displayed.
- NAR is 45 degrees, WIDE is 120 deg.
- Only B-scope modes can be used for A2A. PPI modes are for A2G.
MAN Vc knob
- 12 position: clockwise 0-9, counterclockwise 1 and 2
- Only active when TRACK switch is set to MAN.
- Clockwise 0-9 set closure velocity 0 to 900 kts.
- Counterclockwise 1 and 2 set opening velocity to 100 and 200 kts.
PULSE switch
- 3 position: SHORT, AUTO, LONG
- Normal position: AUTO??
- AUTO mode changes between short and long depending on various factors.
- AIR-GND mode and CAA mode force SHORT mode.
MODE knob
- 6 position: BST, RDR, MAP, AIR-GND, BEACON, TV
- Normal position: RDR for A2A, AIR-GND for A2G
- TV mode not used by this version of the F-4.

A2A modes with automatic tracking:
MODE knob	DISPLAY knob	RANGE knob	SCAN	Nutation?
RDR	B NAR, B WIDE	5 to 50	1 BAR, 2 BAR	yes
MAP	B NAR, B WIDE	5 to 50	forced 1 BAR	no, until tracking