1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

402 - A/A - Pilot - Gun and Sidewinder

Fence In
MASTER ARM ... ON

Best sustained turn ... Sea level: 0.78 Mach/525 KIAS; 35,000 ft: 0.85 Mach/300 KIAS

Gun
1. Station Selection buttons ... GUN station selected
2. Weapon Selector switch ... GUN (Pinky switch up)
3. Sight Mode knob ... A/A
4. Rate of Fire switch ... as desired (center console left), HIGH is 6000 RPM, LOW is 4000 RPM
  - (Auto Clear switch only applies to gun pods. If on, will continue firing briefly after trigger is released to keep chambers clear.)
Optional but recommended: Lock target with CAA mode or Jester.
  - Rear Thumb Button press to enter Cage mode, then Flip-down Trigger press to enter CAA mode. Select scan azimuth with Pinky Switch up/down/press. After lock, Pinky Switch back to desired weapon. Double-press Jester Context button to exit Cage mode.
If target is locked, range indicator on pipper shows 1,000 ft per hash mark, from 1,000 ft at 6 o'clock to 6,700 ft (approx 1.1 nmi).
  - If no target is locked, range will default to 1,000 ft.
Press Trigger to fire.
  - Gun ammo counter is on the center console bottom left.

AIM-9 Sidewinder
1. Sight Mode knob ... A/A
2. Weapon Selector switch ... HEAT (Pinky switch press)
3. Optional but recommended: Lock target with CAA mode or Jester.
  - Rear Thumb Button press to enter Cage mode, then Flip-down Trigger press to enter CAA mode. Select scan azimuth with Pinky Switch up/down/press. After lock, Pinky Switch back to desired weapon. Double-press Jester Context button to exit Cage mode.
1. With locked target:
  1. Range indicator on pipper shows 3,000 ft per hash mark, from 3,000 ft at 6 o'clock to 20,000' (approx 3.3 nmi).
  2. Radar shows Rmax and Rmin lines. Range is valid when target is between the lines.
  3. Sidewinder seeker DOES NOT get slaved to the radar target. The ASE circle only shows the missile boresight and dot for manual aiming reference.
2. Fly to put the target in the missile seeker boresight.
3. When you get tone, optionally uncage by pressing and holding Gray Reset Hat press.
4. Fire with Trigger.

AIM-9 Sidewinder variants
Name	Aspect	Smoke	Notes	In service
AIM-9B	Rear, very limited	High	USAF designation was GAR-8	1956
AIM-9J	Rear	High	Improved AIM-9E	1972
AIM-9JULI	All	??	Made by Germany and used only by Spain. AIM-9J/N/P body with AIM-9L seeker.
AIM-9L	All	High		1977
AIM-9M	All	Low		1982
AIM-9P	Rear	High	Improved AIM-9J. Export and USAF use.	1978
AIM-9P3	Rear	Low	Export and USAF use.
AIM-9P5	All	Low	Export and USAF use. Same IRCCM as AIM-9M.

As far as I can tell, USAF F-4Es never or very rarely carried AIM-9L or M. The best they used was generally the P, maybe the P3. Unknown if they carried the P5. The F-4G did carry L/M though, and F-4Es in foreign service may have carried at least the L and/or P5.