1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

403 - A/A - Pilot - Sparrow

Fence In:
1. Master Arm ... ON
2. RDR MSL switch ... CW ON (T3 switch)

Best sustained turn ... Sea level: 0.78 Mach/525 KIAS; 35,000 ft: 0.85 Mach/300 KIAS

AIM-7 Sparrow
1. Tuning, before engagement:
  1. Radar ... ON, or any position other than OFF
  2. RDR MSL switch ... CW ON for at least one minute
    - The blue "RDR" missile status light should illuminate for at least one minute for each station with a Sparrow. AIM-7E and E2 require 4 minutes, all others require 1 minute.
    - You can set the switch to STBY if you want to safe the Sparrows, but there's no downside to leaving it ON.
1. Setup:
  1. Weapon Selector switch ... RADAR (Pinky switch down)
  2. Sight Mode knob ... A/A
  3. RDR MSL switch ... CW ON (center console)
2. Lock target with Jester commands or CAA auto-acquisition mode.
  - Rear Thumb Button press to enter Cage mode, then Flip-down Trigger press to enter CAA mode. Select scan azimuth with Pinky Switch up/down/press. After lock, Pinky Switch back to desired weapon. Double-press Jester Context button to exit Cage mode.
1. Range indicator on pipper shows 3,000 ft per hash mark, from 3,000 ft at 6 o'clock to 20,000' (approx 3.3 nmi).
2. Radar screen will show two lines: RMax (max range assuming target doesn't maneuver) and RMax2 (max range assuming target maneuvers up to 8G).
  - There is no RMin line for Sparrows, but radar will show a Break X if within min range.
1. If INTERLOCK switch is ON (instrument panel lower), you must be in these parameters to allow launch:
  1. Missile in range (IN RANGE light lit, next to radar screen).
  2. Target aim dot inside the ASE (Allowable Steering Error) circle.
  3. Radar display not in VI (Visual Intercept) mode.
2. Special missile considerations:
  - AIM-7E/E2: If Master Arm switch is ON before radar lock, delay 4 seconds after lock until firing.
  - AIM-7F: If Master Arm switch is ON before radar lock, delay 2 seconds after lock until firing.
  - If Master Arm switch is set to ON after radar lock, subtract 2 seconds from numbers above.
  - This delay is needed in order for the missile to calibrate to the target's doppler shift??
1. When in range, fire with Trigger.
2. After launch, RMax2 line falls to bottom of display and starts going upwards, representing the missile flight time. When line reaches target, missile should as well.

Other information
- Launch sequence:
  - Left forward, right forward, left rear, right rear.
- If you have a centerline tank or certain stores, forward missiles may not be able to launch until tank or stores are jettisoned. If launch is inhibited, CL TK light will illuminate (instrument panel lower)

AIM-7 Sparrow variants
Name	Notes	In service
AIM-7E	Base version.	1963
AIM-7E-2	"Dogfight version", clipped fins for better maneuverability at close range, reduced fuzing time for shorter min range. However, poorer energy retention at long range.	1969
AIM-7F	Improved rocket motor and greater range, solid-state guidance system, larger warhead.	1975
AIM-7M	Improved seeker (look-down/shoot-down), better fuze, better autopilot for optimized trajectory, improved warhead.	1982
AIM-7MH	Improved homing algorithm with lofting ability?	1987
AIM-7P	New fuze, autopilot supports mid-course guidance updates, better against small or low targets.	1993

As far as I can tell, USAF F-4Es never or very rarely carried AIM-7M, MH, or P. The best they used was generally the F. The F-4G did carry at least the M though, and F-4Es in foreign service may have carried M or better.
Selected sources:
- https://www.globalsecurity.org/military/library/policy/navy/ntsp/Aim-7p.pdf
- https://archive.org/details/incendiaries-explosives-and-munitions/U-S-Missiles/page/n3/mode/2up?q=%22aim-7p%22