1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Pilot - Guns, Rockets, Dispensers

Fence In
MASTER ARM ... ON

Gun strafing
1. Setup:
  1. Sight Mode knob ... CAGE, or A/G if using reticle depression
  2. Reticle Depression knob ... as needed
  3. Station Select buttons ... GUN
    - For gun pods: Select gun pod stations.
  1. Fuze switch ... ignored
  2. Delivery Mode knob ... ignored
  3. Weapon Selector knob ... not TV or ARM (any other setting OK??)
  4. AWRU INTRVL and QTY knobs ... ignored
  5. RATE switch ... HIGH or LOW as needed (center console left)
2. Press Trigger to fire.

Rockets
1. Setup:
  1. Sight Mode knob ... A/G, or CAGE for point-blank
  2. Reticle Depression ... as needed
  3. Station Selection buttons ... weapon stations selected
  4. Fuze switch ... ignored
  5. Delivery Mode knob ... DIRECT
  6. Weapon Selector knob ... RKTS & DISP
  7. AWRU INTRVL knob and switch ... as needed
  8. AWRU QTY knob ... as needed:
    - C ... (Continuous ripple) While pickle is held, fires one rocket at a time from the outermost selected stations only, at selected intervals. If only one symmetrical station is selected, fires single rockets from that station.
    - S ... (continuous Salvo) While pickle is held, fires one rocket simultaneously from each selected station, at selected intervals. Cycles through pods on MER if equipped.
    - P ... (Pairs) With each pickle press, fires a pair of rockets from the outermost selected symmetrical stations only. Cycles through pods on MER if equipped. If only one symmetrical station is selected, fires pairs from that station. Fires singles from centerline station. Ignores interval.
    - Numbers 1-18 ... While pickle is held, fires up to N rockets total, one at a time from selected stations, outside in, at selected intervals.
1. Put pipper on target, press Red Button to fire.
2. Accuracy is poor.

Dispensers
CBU-2B/A dispensers with BLU-3B bomblets recommended. Other bomblet types have not been tested.
1. Setup:
  1. Sight Mode knob ... CAGE, or A/G
  2. Reticle Depression knob ... as needed, about 120 mils seems right for ~200 ft, ~450 kts delivery, or just aim halfway between the reticle and bottom of gunsight glass
  3. Station Selection buttons ... weapon stations selected
  4. Fuze switch ... ignored
  5. Delivery Mode knob ... DIRECT
  6. Weapon Select knob ... ROCKETS & DISP
  7. AWRU INTRVL knob and switch ... as needed, 0.01 to 0.05 recommended
    - 0.01 covers about 0.25 nmi, 0.05 covers about 0.5 nmi.
  1. AWRU QTY knob ... S to fire from all dispensers simultaneously, including centerline
    - All other modes fire only from the outermost stations, even if centerline station is also selected.
1. Press and hold Red Button to drop. Dispensers will fire as long as button is held.
2. With low altitude attack (~200 ft, ~450 kts), start dropping when target is halfway between the reticle and bottom of gunsight glass.