1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - Pilot and WSO - AGM-65 Mavericks

Fence In
MASTER ARM ... ON

AGM-65 (all variants) -- Pilot -- Missile setup
1. Sight Mode knob ... A/G
2. Reticle Depression knob ... 45 mils (approx matches Maverick boresight)
3. Station Select buttons ... select Maverick pylons (LI and RI)
4. Fuze switch ... NOSE & TAIL or as needed
5. Delivery Mode knob ... DIRECT
6. Weapon Select knob ... TV
  - Powers on the missile and begins gyro warmup, takes 3 minutes. Use stopwatch to track time.
  - When warmed up, pylon selection buttons should show ARM.
  - Missiles have a max operating time of 30 minutes. To power down, set Weapon Select knob to anything except TV. Warmup will need to be done again if set back to TV.
Display Mode switch ... TV (center console, or T4 button)
- If needed, tell Jester to show the weapon video (he should do this automatically when you switch to TV mode) ... Jester menu -> Air To Ground Weapons -> TV Video -> Weapon
- To alternate pylons when using TERs, start with LI and RI selected, fire a missile or two from the left, then deselect LI to force firing from RI for the next shot. (Don't use the TGT/MSL REJ switch, that only steps through missiles on the same pylon when using a TER.)

AGM-65 -- Pilot -- Attack procedure
AGM-65A/B variants:
1. Roll in on target.
2. Press Trigger to jettison protective cover from missile, uncage the seeker, and start video feed.
3. To slew missile crosshairs: Press and hold Gray Reset Hat press, and use Ministick to slew. When you release Gray Reset Hat press, missile will attempt to lock.
4. When crosshairs are "tight", missile is locked. Usually, if you can lock the target, you're in range.
5. Press and hold Red Button to fire.
AGM-65D/G variants same as A/B variants, except:
Press Trigger to toggle FOV while caged (boresighted) or slewing (holding Gray Reset Hat press).
  - IMPORTANT: If missile is locked, pressing Trigger will cage the seeker (and lose the lock).

AGM-65 -- Pilot -- Abort procedure
AGM-65A/B variants:
Press Trigger to cage the seeker.
  - IMPORTANT: Seeker must be caged before significant maneuvering or risk damage to seeker.
  - Gray Reset Hat and/or Antenna Hand Control Half-Action must be released in order to cage.
AGM-65D/G variants same as A/B variants, except:
As long as seeker is not locked or slewing, it is safe to maneuver?? If seeker is locked, or slewed off boresight, press Trigger to cage seeker.

AGM-65 (all variants) -- WSO controls -- WIP
1. Pilot must set up weapons as detailed above.
2. DSCG Mode knob ... TV (below radar screen)
3. Video Select button ... WEAPON (instrument panel left, button says WEAPON/ASQ-153)
4. Once on attack run and crosshairs are in general vicinity of target:
  1. Press Trigger on flight stick to jettison protective cover from missile, uncage the seeker, and start video feed.
  2. Press and hold Antenna Hand Control Half-Action (Trigger Stage 1), and use Antenna Hand Control stick to slew. When you release Half-Action (Trigger Stage 1), or press Full-Action (Trigger Stage 2), missile will attempt to lock.
  3. To toggle FOV for AGM-65D, press Half-Action when caged or slewing??.
  4. To re-cage, press Half-Action when not slewing??

AGM-65 Maverick variants
- AGM-65A -- TV guided, wide FOV
- AGM-65B -- TV guided, narrow FOV
- AGM-65D -- IR guided, wide/narrow FOV
- AGM-65G -- IR guided, large warhead, wide/narrow FOV