1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start Checklist
Don't rearm/refuel until you're done with the ground crew interaction at the beginning. They can only do one thing at once.
1. BATT switch ... ON (front panel lower right)
2. L GEN and R GEN ... ON (front panel lower right)
3. BOOST PUMPS, LEFT and RIGHT ... ON (front panel lower right)
4. Ground Crew ... Connect compressed air supply
5. Ground Crew ... Apply compressed air
6. When left RPM at 10% ... Left Engine Start button (front panel lower left)
7. Left Throttle ... Idle (Shift-Bottom Thumb Button press)
8. Monitor left engine until 50% RPM
9. Ground Crew ... Apply compressed air (or increase left engine to 95% RPM to provide crossbleed air, use brakes or wheel chocks, then press Right Engine Start to begin spooling up)
10. When right RPM at 10% ... Right Engine Start button (front panel lower left)
11. Right Throttle ... Idle (Bottom Thumb Button press)
12. Monitor right engine until 50% RPM
13. Ground Crew ... Disconnect compressed air supply
14. Ground Crew ... Remove wheel chocks if needed (default is removed)
Now you can rearm/refuel.
1. Canopy ... close
2. Air brake ... Retract (button on virtual throttle is forward for retracted)
3. Flaps ... AUTO (Speedbrake Hat up 2x) (button on virtual throttle is aft for auto)
4. YAW and PITCH Damper switches ... ON (behind throttle)
5. OXYGEN SUPPLY switch ... ON (right console front)
6. OXYGEN DILUTER switch ... NORMAL OXYGEN (right console front)
7. Standby Attitude Indicator ... Uncage and set to same as primary
8. PITOT HEAT ... ON (front panel lower right)
9. ENGINE ANTI-ICE ... Only if needed (below 4 deg C and high humidity) (front panel lower right)
10. RADAR knob ... STBY or OPER (must take off within 10 minutes to avoid overheating)
11. Master Caution ... Reset

Proceed with rest of checklists.