1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Navigation, Landing

Takeoff
1. Nose Wheel Strut ... Extend
2. Begin takeoff run, DO NOT USE NWS OVER 60 KTS, use differential braking until rudder is effective
3. Rotate at 145 to 190 depending on weight.

Navigation
TACAN
1. Set TACAN mode to T/R.
2. Set TACAN freq as needed.
3. Set NAV MODE knob to TACAN.
4. (Optional) Set a course to follow through the TACAN station:
  1. On HSI dial, turn CRS knob to set course line.
  2. White line through center shows course deviation, white triangle on outer dial shows course direction.
5. Distance to TACAN station is shown on HSI dial.
ADF on radio beacon (not the NDBs shown on the map)
1. Set radio mode to ADF.
2. Set radio freq as needed.
3. Set NAV MODE knob to DF.
4. White triangle on HSI shows direction to source, DF flag indicates Direction Finding in use.

Landing
1. Pattern altitude is 1500 ft AGL.
2. Pattern speed is 165 kts.
3. Approach/final speed is On Speed AOA or 145 kts minimum.
  - Formula is Vapproach = 145 + (fuel lbs - 1000) / 200, +5 if you have gun ammo.
  - E.g. 3000 lbs of fuel + gun ammo = 160 kts approach speed.
1. Under 260 kts, gear down.
2. Flaps AUTO.
3. Slow to On Speed AOA (approx 145 to 160 kts) and trim.
4. Adjust pitch with throttle.
5. Aim at end of runway. Approach angle/glideslope should be 3°.
6. Flare at 20 ft. 600 ft/m max descent at touchdown.
7. Deploy drag chute if needed.