1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Cold Start

Cold Start
1. Ground crew ... External electric power ON (backslash, F8, F2, F1)
2. Flight Control switch ... ALTERNATE ON (left) (behind throttle)
3. Throttle ... Full back
4. Engine Master Switch ... ON (right console forward)
5. Battery Switch ... Starter (down) for 2-3 seconds, then Battery (up) (right console forward)
6. When engine RPM is over 3% (small inner dial), Throttle ... OUTBOARD (Bottom Thumb Button)
7. When engine RPM is over 6% (small inner dial), Throttle ... IDLE (Bottom Thumb Button again)
8. When engine RPM is over 25%, Flight Control switch ... RESET for 2-3 seconds, then NORMAL (behind throttle)
9. Hydraulic System Indicator Selector switch ... NORMAL (middle, default) (top row of instrument panel, left of center)
10. Airbrakes ... retract
11. Oxygen Regulator Supply Valve ... ON (small green knob, left wall low, by left knee)
12. Ground crew ... External electric power OFF (backslash, F8, F2, F2)
13. Canopy ... Close (T7 down)

Follow remaining steps in pre-flight checklist on following page.