1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Guns and Sidewinders

Guns -- 6x 0.50 cal
1. Arming knob ... All Guns?? (left wall)
2. Gun-Missile selector knob ... GUNS (center console between legs, right side)
3. Target Wingspan lever ... As needed (MiG-15 = 30 ft)
4. Mechanical Sight ... Uncage (Rear Thumb Button)
5. Max radar range is 1600 ft. Solid red light indicates radar tracking, flickering indicates radar getting returns but not tracking.
6. Electrical Caging button ... Hold for a second, then release (Front Thumb Button). Radar should start tracking target's range.
7. Maneuver in same plane as target and track smoothly.
8. When pipper is on the target, press Trigger to fire.

GAR-8 Sidewinder -- IR seeking, very short range, tailpipe only
1. Gun-Missile selector knob ... MISSILE (center console between legs, right side)
2. Mechanical Sight ... Uncage (Rear Thumb Button)
3. Missile Launch Mode switch ... RH (default) or LH+RH as desired (to left of gunsight)
4. Electrical Caging button ... Hold for a second, then release (Front Thumb Button). Radar should start tracking target's range.
5. When you have tone and target is within 2000 ft, press Red Button to fire.

General dogfighting tips:
- Keep your speed up, 0.61 Mach at sea level to 0.8 Mach at 40,000 ft (best climb speed) or more.
- MiG-15bis vs F-86F:
  - Plane	Accel.	Sust. turn	Roll	Climb	Top speed and dive
  - MiG-15bis	better	better	worse	better (@0.6 M)	worse (0.875 Mach)
  - F-86F	worse	worse	better	worse (@0.61+ M)	better (0.95 Mach)
  - If you're in the MiG: Try to get the F-86 into a sustained level turn fight. If you get pulled into a scissors, break away ASAP and climb away at 0.6 Mach.
  - If you're in the F-86: Use scissors maneuver with your better roll rate to force the MiG out front. If you get pulled into a sustained turn fight, dive away to >0.9 Mach and extend.