1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Basic Navigation, Landing

Shore Takeoff
1. Trim ... Reset to +12° nose up (press Trim Reset button (Trim Hat press), or set manually, see FCS page for current setting)
2. Flaps ... HALF (middle switch position)
3. (Optional) Show best climb speed on HUD. Go to FPAS page (in SUPT menu), press CLIMB button. Best climb speed for current altitude appears above airspeed indicator on HUD (in NAV master mode only).
4. Begin takeoff run.
5. Rotate at approx 150 kts, hold about 7° pitch.
6. Retract gear and flaps when airborne. (Flaps will retract automatically when over 250 kts so can't be damaged by overspeed, but switch should be set to OFF (up).)

Carrier Takeoff
1. Catapults are numbered right to left. 1=front right, 2=front left, 3=waist right, 4=waist left.
2. Do what the yellow shirts tell you to do.
3. Make sure wing fold lever is locked (pushed in), flaps at HALF.
4. (Optional) Show best climb speed on HUD. Go to FPAS page (in SUPT menu), press CLIMB button. Best climb speed for current altitude appears above airspeed indicator on HUD (in NAV master mode only).
5. To avoid CHECK TRIM Master Caution error, set trim based on weight, or use at least 16° (CHKLST page for weight, FCS page for current trim amount). 44k or less lbs = 16°, 45k-48k lbs = 17°, 49k lbs or more = 19°.
6. Use Mil power or AB for takeoff weight under 49k lbs; AB required for takeoff weight of 49k lbs or more.
7. Salute to launch (B3 button).

Basic Navigation (see other pages for adding waypoints and TOT)
Waypoints
1. Select active waypoint in HSI or SA page with up/down arrows on right.
2. Press WYPT button to box it and put waypoint info into the HUD. HUD shows bearing and range in lower right corner, and heading tape shows a marker.
TACAN
1. Press TCN button on UFC.
2. Enter TACAN channel number on keypad and press ENT. Select X or Y to set the channel letter.
3. Select T/R for land-based or carrier navigation, or A/A for air refueling tankers.
4. Press ON/OFF button to turn on TACAN.
5. On HSI page, TACAN bearing and range shows in the upper left corner. Press TCN OSB to put the steering info in the HUD.
To see a full list of all TACAN stations: on HSI page, press DATA button, then TCN. Press HSI to return to HSI page.

Shore Landing
1. Under 250 kts, gear down and flaps FULL.
2. Slow to On Speed AOA (approx 145 to 155 kts, top light=too slow, bottom light=too fast) and trim to put VV level with center of "E" bracket.
3. Adjust pitch with throttle.
4. Aim at end of runway. Approach angle/glideslope should be 3°.
5. Fly it down into the ground, do not flare, 600 ft/m descent at touchdown.
6. After stopping, retract airbrake, set flaps to HALF, and press Trim Reset button (Trim Hat press).

Carrier Landing (minimal procedure)
1. Set TACAN to carrier's channel for approach (see steps above).
2. Set ICLS to carrier's channel for instrument approach guidance. Press ILS button on UFC, enter channel on keypad, press ENT, then press ON/OFF to turn on.
3. Contact carrier on radio and call "Inbound". Carrier will respond with weather, altimeter setting, and BRC (Base Recovery Course, the heading of the carrier itself), ending with "Report see me at 10". Set BRC as a Course in the HSI for reference.
4. Call "See you at 10" when 10 miles out.
5. Fly the pattern (left as an exercise to the reader).
6. Under 250 kts, gear down (T5 switch), hook down (shift-T5 switch), and flaps FULL.
7. Slow to On Speed AOA (approx 145 to 155 kts, top light=too slow, bottom light=too fast) and trim to put velocity vector level with center of "E" bracket.
8. Adjust pitch with throttle.
9. On final turn, call Hornet Ball (B6 button) to get LSO guidance.
10. Put velocity vector about at the crotch of the carrier, where the front of the angled deck meets the main flight deck on the port side.
11. Fly it down to an "OK 3-wire".