1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Advanced Navigation: Markpoints, TOT, Altitude warnings, Bullseye, Beacons

Markpoints -- MK1 through MK9
Press MKn OSB on HSI page to save current designated target as a Markpoint. The markpoint number will be incremented automatically after saving, wrapping from MK9 back to MK1.
  - If you have no designated target, markpoint will be created at your current flyover location.
  - There is no way to cycle back through the MKn numbers without overwriting all the points you cycle through.
1. To select a saved markpoint for navigation or targeting, use the Waypoint Inc/Dec OSBs. Markpoints are saved in order before regular waypoints, so use Previous Waypoint down past waypoint 0 (or up past waypoint 59) to get to the Markpoints. SEQn OSB must be un-boxed.
2. Markpoints work basically like waypoints, and can be designated for targeting using WPDSG. For instance you can designate several markpoints through the tpod at high altitude and long distance, then get low and do toss attacks against those points.

Set TOT (Time On Target)
1. In HSI page, press DATA OSB; will show current waypoint sequence with current waypoint selected.
2. Press SEQ UFC OSB (left side bottom).
3. On UFC, press TGT OSB, enter number of waypoint you want to set as the TOT waypoint.
4. Press TOT OSB, enter time in HHMMSS Zulu time, then ENT. You can see current local time on the IFEI engine monitor, and current Zulu time in the HUD.
5. Optional: Press GSPD OSB, enter ground speed in kts. This is the speed you want to fly from the waypoint before the TOT waypoint, to the TOT waypoint.
6. Press HSI OSB to return to main HSI page.
7. HSI will now show the required ground speed to meet the TOT. HUD also shows symbology for ahead/behind TOT under airspeed number. Caret to left of vertical line means you're slow/late, caret to right of vertical line means you're fast/early.
8. You can use Auto Throttle Control (ATC) (Pinky Switch press, shows ATC in HUD) to hold your current speed.

Altitude Warnings -- Bitchin Betty "Altitude, Altitude" audio
1. In HSI page, press DATA OSB; will show current waypoint sequence with current waypoint selected.
2. Press A/C UFC OSB (top row left).
3. Altitude warnings are on bottom row: BARO, RADAR (not implemented), and TAWS.
  - BARO sounds "Altitude, Altitude" warning when you go below that barometric altitude. Useful for setting a hard deck for SAMs or AAA.
  - RADAR sounds warning when you go below that radar altitude. This is separate from the Radar Altimeter siren audio for the altitude set on the Radar Altimeter gauge.
  - TAWS boxed or unboxed sounds the "Pull Up" and "Roll Right/Left" warnings when you're about to fly into the terrain.

Bullseye waypoint
1. In HSI page, press DATA OSB; will show current waypoint sequence with current waypoint selected.
2. Use Waypoint Inc/Dec OSBs to select waypoint to edit.
3. Press A/A WP OSB to box it and set the selected waypoint as bullseye.

Navigate to a beacon
- Pick either radio and set its ADF switch to On on the UFC.
- Set radio to any channel, or M for manual, and tune ADF frequency. Radios can tune to any frequency from 108.0 to 400.0.
- HSI page will show a circle outside the compass which is the heading to the ADF beacon.