1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - Radios, Datalink, HMD options

Radio setup and tuning
Band	Frequency range	Modulation	T/R	Notes
COM1 and COM2 -- ARC-210
VHF	30.000 to 87.995 MHz	FM	T/R
VHF	108.000 to 117.995 MHz	AM	R
VHF	118.000 to 135.995 MHz	AM	T/R
VHF	136.000 to 155.995 MHz	AM/FM	T/R
VHF	156.000 to 173.995 MHz	FM	T/R
VHF/UHF	225.000 to 399.975 MHz	AM/FM	T/R

Using preset frequencies:
1. Rotate COMM1 or COMM2 volume knob on UFC to select channel. Selected channel is shown in readout above volume knob.
2. Each radio has 20 preset frequencies (1-20), Manual (M), Guard (G), Cue channel for SINGARS (C), and maritime (Sea) channel (S).
Changing preset frequencies:
1. Select desired preset channel to change.
2. Enter new frequency on UFC and press ENT to store, which overwrites previous frequency.
Using manual frequencies:
1. Tune radio to M channel.
2. Enter frequency on UFC and press ENT.
3. Or, just tune to any unused numbered channel and store the new frequency in that channel.

HMD options -- Configuring the JHMCS
Set the max range at which the HMD will show targets:
  1. Press MENU OSB 2x to go to SUPT page.
  2. Press HMD OSB (L3), then MIDS SETUP OSB (B4), then set range with up and down arrow OSBs (R4 and R5). Can go up to at least 100 nmi.
More TODO...