1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - Datalink (TNDL/Link16) for F-18

General info
- Link16 datalink must be ON (D/L button 2x on UFC, then press and hold ON).
- Team Members and Donors can be changed in flight.
- Team Members share contacts and targets, Donors share only contacts.
- You can have up to 4 Team Members and up to 8 Donors.

Sending targets/SPIs to Team Members
On SA page, if TXDSG OSB is boxed (default), your current target is always shared to all Team Members.

Receiving target/SPI from Team Member and using it as your target
- On SA page, all Team Members' current targets are automatically shown with dotted line to the Member who locked the target. They also shown in the HMS with an icon.
- If you lock an air target that is also locked by a Team Member, the target designator diamond will have a caret ("^") over it, aka a "hat".
- To lock a Team Member's ground target, manually slew the TPOD using the marker on the SA page or HMS, or visually designate on the icon with the HMS.

Changing Team Members
- On SA page, set SOI, then move cursor over a friendly plane, or use STEP OSB to cycle through all contacts on SA page.
- The MEMBn or DONRn OSB will be boxed if the plane is a Member or Donor respectively. Press the respective OSB to set or unset the selected plane. The n shows what number they are (if boxed) or will be assigned to (if unboxed).
- On SA page, Team Members are shown with a dot at 9 o'clock and a letter inside the circle. Donors are shown with a dot at 9 o'clock only (no letter).

Get your own STN (needed for other non-F-18 planes to add you as a Team Member)
- Go to TAC menu page, then TGT DATA OSB, then GROUP OSB.
- Ownship callsign is shown in the top row of the top box, VCS column.
- Ownship STN is shown in the top row of the bottom box, TN column.