1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start Checklist -- Auto Start is much slower
1. BTRY ... ON (rear overhead panel)
2. APU STOP/RUN/START knob ... START and hold until green light comes on, then release to RUN (front overhead panel)
3. EXT PWR knob ... APU (rear overhead panel)
4. BLEED AIR, APU button... OPEN (press to turn on, should stabilize at 40.0 PSI) (front overhead panel)
5. AUX PUMP switch ... ON (turns on hydraulic system) (copilot, lower instrument panel)
6. ENGINE 3 START knob ... START and hold until green light comes on (front overhead panel)
7. EXT PWR knob ... OFF (rear overhead panel)
8. APU STOP/RUN/START knob ... STOP
9. ENGINE 2 START knob ... START and hold until green light comes on (front overhead panel)
10. ENGINE 1 START knob ... START and hold until green light comes on (front overhead panel)
11. ENGINE 4 START knob ... START and hold until green light comes on (front overhead panel)
12. Doors and windows ... Close:
  1. Cockpit windows ... LShift-D
  2. Crew entry door ... LCtrl-D
  3. Paratroop doors (side doors) ... LAlt-D
  4. Cargo ramp and door ... LCtrl-C
13. Pilot and Copilot HUD ... Deploy (knob on side of HUD hinge)
  - Adjust shading as needed (HUD BRT knob on far front left/right overhead panel)
More??