1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Basic ABRIS Navigation, Countermeasures

Set a navigation destination in ABRIS -- USE THIS METHOD TO QUICKLY SET A DESTINATION
1. Press OSB 5 until you cycle to NAV page. Press MAP OSB, then INFO OSB. This centers your position on the map and enables a cursor.
2. Move the cursor on the map with the lower right knob on the ABRIS. Right-click the knob to toggle between moving left/right and up/down. Lat/Long is shown for the cursor location.
3. Press SCALE+ and SCALE- OSBs to zoom in and out, and recenter the map on the cursor.
4. When the cursor is over your destination, press INFO OSB again, then press TO OSB to set a direct course.
5. The DTA (Desired Track Angle), DST (Distance), and ETA is shown in the bottom center panel of the ABRIS. Your current track angle is shown at the top center.
6. Press SUSP OSB to cycle between showing route from start to destination, and destination to start.
7. (Optional) Set ABRIS map grid to MGRS (100 km squares and 10 km squares):
  1. OSB 5 to return to main screen, then MENU > OPTION > CHARTS, scroll down to the bottom past "LINE OBJECTS" to ГEO. CETKA (lat/long grid) and UTM CETKA (MGRS grid). Press OSB 5 to page directly to the map.

UV-26 Countermeasures system
1. Left switch sets dispenser sides (left/both/right). Lights on display indicate selected side(s).
2. Right switch toggles between showing number of flares remaining, and flare program.
3. In flare program mode, display shows current program:
  - 1st number: Number of dispensing pulses
  - 2nd number: Number of flares per pulse
  - 3rd number: Number of seconds between pulses
1. Press NUM button (upper left) to increment 1st number (number in parens indicates actual number dispensed, e.g. 5=12 flares dispensed).
2. Press SEQ button (middle left) to increment 2nd number.
3. Press INT button (upper right) to increment 3rd number (number in parens indicates actual interval delay, e.g. 7=0.25 seconds).
4. Press RESET PROG button (middle right) to reset to default values (110).