1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - All

Master Arm ... ON
Weapon launch mode ... Manual
Laser designator ... Armed
HMS ... ON (Coll Index Finger Hat up)

Lock a target with Shkval
1. Press Coll Index Finger Hat forward to toggle HMS sight.
2. Press and hold Shkval uncage (Coll Trigger 1st stage) to turn on Shkval TV monitor and slave Shkval to HMS. Let go of Shkval uncage button when looking at or near target.
3. Set Shkval target frame size (Coll Middle Hat left/right) (usually smallest seems best).
4. Set Shkval zoom (Coll Middle Hat forward/back).
5. Use Coll Ministick to slew target frame over target, press Coll Ministick press to laser range and lock. You may get a ground lock ("ТГ" on upper left of Shkval) or a contrast lock ("TA" on upper right).
6. Both types of locks can guide/direct weapons. Contrast locks are more reliable, but may not be achievable in other than bright and clear weather, except at close range.
  - Ground locks may sometimes lose their lock and the Shkval can start drifting around. Re-lasing periodically (every 5 to 15 seconds) can help it keep the lock. Fast flight or maneuvering can also cause it to lose the lock. If it gets really goofed up, try resetting the targeting system (Coll Index Finger Hat 3 back) and then Coll Ministick press to lock the target again.
1. Once laser-ranged, it will use triangulation and your doppler system from then on to calculate the range. That means the range may not always be accurate. Doesn't matter for the beam-riding Vikhrs, but for cannon accuracy you may need to re-lase frequently.
2. Your laser will eventually overheat, but it should take quite a while, since it's not in continuous operation unless it's guiding a missile, or you're hitting the lock button constantly.
3. To unlock, press and hold Coll Ministick press and slew in any direction.

9K121 Vikhr (AT-16 Scallion) ATGM
(Note: ATGM Temperature knob on right rear wall has no function in game.)
1. Select Vikhr missiles (Gray Reset Hat left for outboard stations). This should make a launch circle appear on your HUD.
2. Stores panel under Shkval should say "ПC"; first number is how many missiles you have left, second number is cannon rounds x10.
3. Lock target with Shkval as described above.
4. Vikhrs range is 8.0 km/4.3 nmi max, 800 m/0.4 nmi min. (You can go up to 9 km/4.9 nmi or more if you're shooting down.)
  - You can use A/A mode (Coll Trim Hat left) to make the missile trigger with a 5-meter proximity fuse at or just past the target, or A/A Head On (Coll Trim Hat right) to trigger the proximity fuze just before the target.
  - Ground and ocean don't set off the prox fuse, but some trees or buildings may. Prox-fused missiles should still kill light armor up to BTRs, but are ineffective against tanks.
1. Once you are locked and in range, put the Vikhrs launch circle on the HUD over the target circle, press and hold Red Button to fire. You can still fire even if the circles aren't lined up (as long as Weapon Mode switch is set to Manual), but the missile may waste energy trying to get back into the laser beam, and may weave around excessively.
2. When finished, reset targeting system (Coll Index Finger Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.

2A42 Cannon -- 30 mm, 220 rounds AP, 240 rounds HE
1. Select Cannon (Gray Reset Hat back). Cannon slew limits rectangle will appear on HUD.
2. Stores panel under Shkval will show number on far right, which is rounds x10 for current ammo type.
3. Set cannon burst length, ammo type, and ROF switches (center console under stores panel) (Dish Hat left for ammo type, Dish Hat right for ROF)
Using Shkval targeting system for automatic tracking
Lock target with Shkval as described above.
  - Cannon range is about 3.5 km/1.9 nmi max, although accuracy will be poor at that range. Re-lase frequently to make sure the range doesn't drift.
1. Once you are locked and in range, put the target circle inside the cannon slew limits rectangle on the HUD. Fire with Trigger.
2. When finished, reset targeting system (Coll Index Finger Hat down) and deselect cannon (Gray Reset Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.
Using boresight mode for manual aiming
1. Set Autotracking switch to TS (Dish Hat press to toggle) (left console next to laser designator arming switch)
2. HUD will show cannon pipper fixed in place. Shkval will show image boresighted to gun pipper.
3. Put pipper on target and fire with Trigger.
4. When finished, reset targeting system (Coll Index Finger Hat back) and deselect cannon (Gray Reset Hat back). That will deselect all weapons, turn off the Shkval, and reset the HUD to nav mode.