1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - L-39ZA Bombs, Rockets

Fence In
1. All weapon CB switches on center console top ... On
2. Weapons Safety Cover ... Down (Flip-down Trigger press, tab on front of stick flips down to engage trigger)

Weapon notes
1. Trigger fires all weapons.
2. Must be faster than 310 kph (170 kts) to fire weapons.
3. When using guns or rockets, throttle is cut automatically while trigger is pulled to prevent flameout due to gas ingestion. RPMs will continue to drop as long as trigger is held.

Rockets -- S-5KO, 16-round pods
WEAPON CARRIER pushbuttons ... Select rocket pylons (left button is outer, right button is inner)
  - Both pylons can be selected at once; if different weapons are loaded, only outer pylons will fire.
  - To deselect a pylon, press the small gray button below the white pushbutton.
MISS. TRAIN salvo switch ... As desired (left instrument panel):
  - MISS. TRAIN -- All rockets ripple fire as long as trigger is held
  - 2 -- 2 rockets fire with each press
  - 4 -- 4 rockets fire with each press
    - Quick presses of the trigger can fire fewer rockets in all modes.
1. Set gunsight depression (see tables on other page); 15 deg seems reasonable for short range attacks (while rocket motor is still burning).
2. Fire with Trigger.

Bombs
WEAPON CARRIER pushbuttons ... Select bomb pylons (left button is outer, right button is inner) (Gray Reset Hat left/right to select, shift-left/right to de-select)
  - Both pylons can be selected at once; if different weapons are loaded, only outer pylons will fire.
  - To deselect a pylon, press the small gray button below the white pushbutton.
BOMBS switch ... As desired (left instrument panel):
  - Without MERs:
    - TRAIN (up) -- Drops all bombs as long as trigger is held, alternating pylons, outer first, then inner, with 0.15 sec interval.
    - 1 (middle) -- Drops one bomb per press from outer pylons, then both bombs at once from inner pylons.
    - SALVO (down) -- Drops all bombs simultaneously.
  - With MERs (OFAB-100 Jupiter parachute-retarded bombs):
    - TRAIN (up) -- Drops all bombs, alternating pylons, outer first, then inner, with 0.15 sec interval.
    - 1 (middle) -- Drops single bomb per press, alternating pylons, outer first, then inner
    - SALVO (down) -- Drops 1 bomb from all selected MERs simultaneously (full load of 4 MERs gives 2 pickle presses)
1. Set gunsight depression (see tables on other page)
2. Fire with Trigger.
OFAB-100 notes
1. Minimum altitude to avoid damage is around 20 m AGL regardless of speed (can go slightly lower if very fast, but never below 10 m). Minimum speed is 350 kph at 20 m.
2. Bomb spacing with 0.15s interval (TRAIN mode):
Speed (kph)	Spacing (m)			Spacing (ft)
	Single	String of 4	String of 8	Single	String of 4	String of 8
310	12.9	51.6	103.3	42.4	169.5	339.0
350	14.6	58.3	116.7	47.8	191.4	382.8
400	16.7	66.7	133.3	54.7	218.7	437.4
450	18.8	75.0	150.0	61.5	246.1	492.1
500	20.8	83.3	166.7	68.3	273.4	546.8

Max speed at sea level with 8x OFAB-100 is about 475 kph.