1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - Gunsight depression tables

Data from the manual, not sure how accurate this is...

Bombs
Dive angle	20 deg	30 deg	40 deg
Gunsight depression	13 deg	11 deg	10 deg
Dive entry alt	1200 m	1500 m	1800 m
Dive entry speed	440 kph	350 kph	300 kph
Release alt	730 m	800 m	1100 m
Release speed	570 kph	550 kph	560 kph
Engine RPM (N1)	97%	92%	?? idle??

Rockets
Dive angle	20 deg	30 deg
Gunsight depression	2.30 deg	2.53 deg
Dive entry alt	1200 m	1200 m
Dive entry speed	400 kph	300 kph
Release alt	500 m	600 m
Release speed	560 kph	550 kph
Slant range	1460 m	1200 m