1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

103 - Controls - Throttle Base
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Mode selector -- Radar power
- 1/2: Radar Power PCH Warm-up (WARM-UP) (takes 3 minutes, no need to map Radar OFF)
- 3: Radar Power SIL Standby (STBY)
- 4: Radar Power EM On (EMIT)
- 5: --
Flaps lever
Axis: --
T1 switch
F: Flashlight toggle
T2 switch
F: Selective Jettison OPEN&ON else CLOSED (doesn't actually jettison, but arms the selective jettison switch)
T3 switch
F: Radar PPI mode (wedge), else B-Scope mode (square, bottom distorted outward)
T4 switch
F: TDC mode Z (directly control antenna elevation), else S (set altitude, elevation changes as needed)
Lighted Buttons -- Master Modes, Master Arm, carrier calls
B1: Gun arm toggle	B2: Master Arm Toggle	B3: FBW G-limiter toggle
B4: Waypoint Decrement	B5: Waypoint Increment	B6: TOT/PAR button toggle
T5 switch -- Landing Gear
- U: Landing Gear up
- D: Landing Gear down
- S-D: Drag chute deploy (Only available if not using ECLAIR countermeasures pod)
T6 switch -- Air Refueling switch
- U/D: -- (no manually controlled flaps)
- S-U: Air refueling transfer switch ON (DAY)
- S-D: Air refueling transfer switch OFF
T7 switch -- Canopy
U: Canopy up/down toggle
E1 dial -- Kneeboard
- P: Kneeboard toggle
- L/R: Flip pages
- S-L/S-R: RWR volume
E2 dial -- NVGs
- P: Toggle NVGs on/off (only if enabled in Mission Editor; NVGs will be visible stowed above left instrument panel)
- L/R: NVG gain up/down