1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing

Takeoff
1. Check canopy closed, speedbrakes closed.
2. Taxi to takeoff position, brakes will hold full mil power.
3. Take off with full afterburner.
4. Rotate around 130 kts. Put inverted T symbol on horizon for 13 degree pitch up to avoid tailstrike.
5. Gear up before 260 kts.
6. Best climb speed is 0.80 Mach (heavy) to 0.90 Mach (clean).
  - Mach shows on HUD once you're over Mach 0.60.

Landing
1. PCA ... APP (approach) (panel above left knee), shows yellow "S".
2. To use precision blind approach system with airport outline: -- WIP
  1. Tune ILS to airport ILS frequency.
  2. Set altimeter to airport QFE??
  3. If you already have a waypoint at the airport, that should be all you need. If you don't have a waypoint:
    1. Select a blank (all zeros) waypoint as PREP waypoint.
    2. Set INS mode knob to CP/PD (cap désiré/pente désirée, desired heading and glideslope)
    3. Left numbers are CP, right numbers are PD. Enter true (not magnetic) runway heading for CP, and 3.0 for PD (standard 3 degree glideslope)
    4. Select current PREP waypoint as DEST.
3. Under 230 kts, put down landing gear.
4. Put velocity vector where you want to land.
5. Throttle as needed to keep accel. chevrons within the approach AOA brackets, about 150-160 kts.
6. Pitch trim as needed to keep velocity vector in AOA brackets, about 14 degrees.
7. Maintain AOA on landing for aerobraking.
8. At 110 kts press Autopilot Standby Mode (Lower Gray Button) to reset trim and allow nosewheel to come down. If you don't press the button, you'll get a Master Caution light and beep. Press the Autopilot Standby Mode button at any time to clear the caution.
9. Apply brakes, retract speedbrake, engage NWS under 40 kts.