1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Radios, Countermeasures, Autopilot, Jettison

Radios
COM1	TRT ERA 7000	V/UHF	118.0 to 149.970 MHz / 225.0 to 400.0 MHz	Preset channels or manual tune.
COM2	TRT ERA 7200	UHF	225.0 to 400 MHz	Preset channels only.

- Radio panel is on left console front, next to left knee. COM2 is the most forward, COM1 is just aft (with the number keys and digital display).
- Tune COM1 to a custom frequency by setting the small knob on the left of the number keys to FF (Fixed Frequency), then enter frequency (to set 253.500, enter 25350), then press VLD button.
- Tune COM2 by turning the chunky black knob on the right to a preset channel.

Countermeasures modes
Chaf﻿f and f﻿lares
CM Hat forward is PANIC deploy, CM Hat aft is selected program deploy.
- Standard load is 16 flares and 112 chaff. ECLAIR pod allows 32 flares and 130 chaff, but no drag chute.
- Modes 1, 2, 3 -- 6 chaff at 0.5 sec intervals, 1, 2, or 3 cycles respectively spaced 2 seconds.
- Mode 4 -- 1 flare only
- Mode 5 -- 1 chaff and 1 flare only
- Mode 6 -- 12 chaff at 0.75 sec intervals, 1 cycle
- Mode 7 -- 20 chaff at 0.25 sec intervals, 1 cycle
- Mode 8 -- 6 flares at 0.25 sec intervals, 1 cycle
- Mode 9 -- 20 chaff and 6 flares at 0.25 sec intervals, 1 cycle
- Mode 10 -- Flare jettison, 32 flares at 0.05 sec intervals, 1 cycle
- PANIC -- 6 chaff and 3 flares, 0.5 sec intervals, 1 cycle
Sabre ECM jammer system
- ECM system has 3 modes (change with EW Mode Selector knob):
  - STBY -- ECM is in standby, passive receive mode
  - Square -- Automatic radar-priority jamming. Jamming is activated automatically, but at lower power that still allows radar operation. PCM jamming (full power, turns off the radar) can be activated manually with Top Hat press.
  - PCM -- Automatic jammer-priority jamming. PCM jamming is activated automatically, radar will turn off while jamming.
- When ECM system is jamming in radar-priority mode, ECM light on RWR is lit. When jamming in jammer-priority mode, "PCM" shows steady in the center of the RWR, radar turns off.
- When countermeasures system thinks you should be jamming in PCM mode, "PCM" will flash in center of RWR (and on HUD and radar screen??)
- According to the manual, DCS doesn't support targeted jamming or different jamming power levels, therefore jamming effectiveness is "similar" in both PCM and Square modes.

Autopilot -- WIP
- Autopilot panel is on the left eyebrow, just under the dashboard sunshield.
- Engage by pressing the PA button twice (leftmost button). First time arms the autopilot system, second time engages it.
- ALT button is level hold. Use trim hat to direct autopilot altitude and bearing when engaged.
- ALT AFF button is selected altitude hold. Set altitude on drums under autopilot panel.

Selective Jettison
1. Master Arm ... ON (B2 press to toggle)
2. Selective Jettison Cover and Switch ... Open and ON (left) (left of PCA panel above left knee)
3. Select stores on PCA. RP = Fuel Tanks
4. Press Red Button to jettison.
5. Selective Jettison Cover and Switch ... OFF and Closed (left of PCA panel above left knee)
6. Emergency Jettison Button to left of left knee will jettison all but outboard Magic missiles. Master Arm must be ON for Emergency Jettison.
7. Full internal fuel is 3160 kg.