1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - CCIP Bombs

Fence In
1. Master Arm ... ON (B2 button to toggle)
2. Radar ... EMIT (Mode knob to 4)
3. Gun arming switch ... ARM (B1 button to toggle)
4. Bomb fuzing, quantity, interval ... Set (PPA, above right knee)

Mixing weapons
- Can have bombs, and rockets on inner wing pylon only. Rockets on outer wing pylon can be fitted but cannot be selected, so is not valid.
- Cannot mix A/G weapons with Super 530D missiles, only Magics.

SAMP-250 note
As of 06/2022, SAMP-250 LD (slick) bombs don't have the right release profile and will always hit long. SAMP-250 HD (parachute retarded) works correctly.

CCIP Bombs -- Mk 82 Snakeye, Mk 82 AIR, SAMP-250 HD, BAP-100 (see below), BLG-66 Belouga
1. Press Gray Reset Hat press ("CNM Switch neutral").
2. On PPA (above right knee):
  1. Bomb Fuze Selector switch ... RET (delay Snakeye fuze/Belouga opening) or INST (instant Snakeye fuze/Belouga opening)
  2. Bomb Release Quantity Selector switch ... At least 1, or as desired. If 0, no bombs will drop.
  3. Bomb Release Interval Selector switch ... As desired, distance in meters
For release timing for BAP-100 anti-runway bombs in order to cover a whole runway, see below.
1. On PCA (above left knee):
  1. Select BF1 for Snakeye or AIR, BF6 for Belouga, BF8 for BAP-100
  2. Select TAS and RS (Radar should be set to EMIT and Radar Altimeter should be ON).
2. Dish Hat up ("Weapons System CMD FWD") to set HUD to BF mode.
3. Put CCIP pipper on target or where you want the string of bombs to start and press and hold Trigger to drop bombs.
  - The small gap in the bomb fall line shows where the last bomb in the string will drop with the current interval setting.
  - Bombs will still drop even if you have the X on the HUD, so be careful.
Set HUD back to NAV mode with Dish Hat down ("Weapons System CMD AFT").
BAP-100 anti-runway bombs
- You need to press and hold Trigger when CCIP pipper is at the beginning of where you want the string of bombs to start. Bomb release line will start moving up from the bottom of the HUD, bombs start releasing when line reaches velocity vector. Keep holding trigger until all bombs are gone.
- Release timing calculation: (Desired bomb string length in nmi * 185.2) / # bombs = interval in tens of m
- For 18 bombs, bomb string length in nmi is ≅ interval / 10, so interval of 15 is 1.5 nmi string.
- Max interval is 28 (280 m) so max string length is:
  - 18 bombs @ 28 = 5040 m / 2.72 nmi
  - 12 bombs @ 28 = 3360 m / 1.81 nmi
  - 8 bombs @ 28 = 2240 m / 1.21 nmi
  - 6 bombs @ 28 = 1680 m / 0.91 nmi
  - 4 bombs @ 28 = 1120 m / 0.60 nmi