1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Radios, Flight Director, Jettison

Radios
COM	Radio model	Freq band	Freq range	Freq step	Notes
COM1	AN/ARC-150(V)2/HQ	UHF-AM	225.000 to 399.975 MHz	25 kHz
COM2	SRT-651/N	VHF-FM	30.000 to 87.975 MHz	25 kHz
		VHF-FM	156.000 to 173.975	25 kHz
		VHF-AM	108.000 to 155.975	25 kHz	See below
		VHF-AM	118.000 to 136.9917	8.33 kHz	Smaller steps in this sub-range
		UHF-AM/FM	225.000 to 399.975	25 kHz

Change transmitting radio with COMM1/COMM2 knob on ICS panel (right console far forward).
COM1 radio
- Radio controls are on the left console, forward radio.
- Power on by setting Function Dial to MAIN or BOTH.
- Using presets:
  1. Mode knob ... PRE
  2. Change channel with Channel knob (just forward of frequency knobs).
    1. Selected channel is shown in window to right of knob, 20 channels available.
    2. Channel and associated frequency are shown on the display on the left upper instrument panel.
Manual frequency tuning:
1. Mode knob ... MAN
2. Set frequency with selector knobs.
COM2 radio
- Radio controls are on the left console, rear radio.
- Power on by setting Function knob to T/R or TR+G
- Using presets:
  1. Mode knob ... PRE
  2. Change channel with switches on right (inboard) side of panel.
    - Selected channel is shown in display above switches, 99 channels available.
    - Channel and associated frequency are shown on the display on the left upper instrument panel.
- Manual frequency tuning:
  1. Mode knob ... MAN
  2. Set frequency with switches below frequency display.

Flight Director
- TODO (not currently implemented)
- NOTE: Flight Director is not an autopilot, it just provides steering indicators.

Jettison -- TODO